## Slide 1: Advanced Modulation Techniques for Telemetry
A Short Course at the
International Telemetering Conference
Las Vegas, NV • October 23, 2017
Terry Hill, Quasonix

## Slide 2: Course Outline
Performance Metrics
Continuous Phase Modulation (CPM)
  Tier 0
  Tier I
  Tier II
Demodulation
  Synchronization
Channel Impairments
  Adjacent Channel Interference
  Lunch
  Multipath Propagation
Impairment Mitigation Techniques
  Diversity Combining
  Adaptive Equalization
  Best Source Selection
  Space-Time Coding
  Forward Error Correction (FEC)
Using All the Tools Together
Performance Comparison & Summary

## Slide 3: Performance Metrics
Information Fidelity
  Additive White Gaussian Noise (AWGN) channels
    Bit Error Probability (BEP) or Bit Error Rate (BER)
  Bursty (dropout) channels
    Cumulative error count
    Link Availability
Bandwidth Efficiency
  Power spectral density
  Fractional Out-of-band Power
  Channel spacing with adjacent channel interference (ACI)
Bandwidth-Power plane

## Slide 4: BER Performance Comparison

## Slide 5: Cumulative Error Counts in Bursty Channels
Figure from Robert Jefferis, Tybrin, Edwards AFB. Reprinted by permission of the author.

## Slide 6: Performance Metrics
Link Availability (LA) – % of the time that the instantaneous BER over 1 sec blocks is less than 10-5.
Video Availability (VA) - % of time video is available (picture on time/ total time x 100)
These two metrics are not the same. Video system sensitivity and its response to bit errors can have significant impact on VA performance.

## Slide 7: Which Bandwidth?
Fixed level
  -60 dBc is common
  -25 dBm is “standard” in IRIG-106
Fractional out-of-band power
  99%, 99.9%, 99.99% are all used
Minimum frequency separation
  Accounts for receive-side effects
    Receiver IF filtering
    Demodulator interference tolerance
    Relative levels of interfering signals
    Depends on application

## Slide 8: Power Spectral Density (PSD)

## Slide 9: Fractional Out-of-band Power
5 Mbps

## Slide 10: Bandwidth-Power Plane
Simultaneous representation of
  Bandwidth Efficiency (Bandwidth normalized to Bit Rate)
  Power Efficiency (Eb/No required to achieve 10-5 BEP)

## Slide 11: Today’s Modulation Tour

## Slide 12: Continuous Phase Modulation

## Slide 13: The Modulation Universe
Analog, Digital
Amplitude modulation
Quadrature amplitude modulation
Angle modulations
  Frequency modulation
  Phase modulation

## Slide 14: Angle Modulations
Includes both frequency modulation and phase modulation
Some have an amplitude modulation component
  BPSK
  QPSK
  Offset QPSK
Some are constant envelope
  Binary FM
    FSK, MSK, premod filtered MSK, GMSK
  M-ary FSK
  SOQPSK
  Multi-h continuous phase modulation
  No amplitude variation
Saturated power amplifiers are ideal for constant envelope waveforms

## Slide 15: Saturated Power Amplifiers
DC-to-RF conversion efficiency is important
  Minimizes cooling requirements
  Maximizes battery life
Maximizing efficiency demands nonlinear operation
Non-linear operation creates AM-AM and AM-PM conversion:

## Slide 16: Constant Envelope Modulations
Before ARTM (Tier 0)
  PCM/FM
  “Legacy” waveform for telemetry
Advanced Range Telemetry (ARTM) Program
  ARTM Tier 1
    Proprietary Feher-patented FQPSK
      FQPSK-B, Revision A1
      FQPSK-JR
    SOQPSK-TG
      Equivalent in performance to FQPSK
      Non-proprietary
  ARTM Tier 2
    Multi-h CPM (M=4, L=3RC, h1 = 4/16, h2 = 5/16)
PCM/FM, SOQPSK and Multi-h CPM are all continuous phase modulations (CPM)

## Slide 17: CPM Notation and Parameters
Where i represents an M-ary symbol sequence
  i derived from input bits di
h is the modulation index
g(t) is the frequency pulse shape in the interval 0 < t < LT
  L = 1 is “full response” signaling
  L > 1 yields “partial response”
CPM is a modulation with memory due to the constraint of continuous phase. Further memory is introduced with L > 1.
-< t <+

## Slide 18: Key Parameters of CPM
M – Order of Modulation (2-ary, 4-ary, etc.)
g(t) - Frequency Pulse (Rectangular, Raised Cosine, etc.)
L – Length of Frequency Pulse
h – Modulation Index
Increase Spectral Efficiency by
  Increasing M
  Reducing h
  Increasing L
  Choosing Smoother Frequency Pulse Shape
In general, increasing spectral efficiency decreases detection efficiency

## Slide 19: CPM Characteristics
Continuous Phase
Constant envelope
Signals are described by their phase trajectories
  Phase tree representation is complete
PSD and BER can be “traded” by
  Varying h, modulation index
  Changing g(t), the frequency pulse shape
Phase trellis decoder is optimum for any variant of CPM

## Slide 20: Phase Tree Representation

## Slide 21: M=2, h=1/2, 1REC (MSK)
PSD vertical axis is dBc per FFT bin
1 FFT bin = 1/64 * symbol rate

## Slide 22: M=4, h=1/4, 1REC
PSD vertical axis is dBc per FFT bin
1 FFT bin = 1/64 * symbol rate

## Slide 23: M=4, h=1/4, 1RC
PSD vertical axis is dBc per FFT bin
1 FFT bin = 1/64 * symbol rate

## Slide 24: M=4, h=1/4, 2RC
PSD vertical axis is dBc per FFT bin
1 FFT bin = 1/64 * symbol rate

## Slide 25: M=4, h=1/4, 3RC
PSD vertical axis is dBc per FFT bin
1 FFT bin = 1/64 * symbol rate

## Slide 26: Multi-h CPM
Cyclically rotates through multiple “sets” of FSK tones
Increases minimum distance in trellis
  Improves BER performance
Widely proposed for high-performance nonlinear channels
  MIL-STD-188-181B

## Slide 27: M=2, h1=1/4, h2=1/2, 1REC
PSD vertical axis is dBc per FFT bin
1 FFT bin = 1/64 * symbol rate

## Slide 28: M=4, h1=4/16, h2=5/16, 3RC
PSD vertical axis is dBc per FFT bin
1 FFT bin = 1/64 * symbol rate
ARTM Tier II Waveform

## Slide 29: CPM Summary
To reduce bandwidth of a CPM signal, the phase transitions must be smoothed by:
  Requiring phase to have more continuous derivatives
  Spreading the phase change over more intervals (i.e., L > 1)
  Reducing h
The shape of g(t) determines the smoothness of the information-carrying phase
An endless variety of CPM schemes can be obtained by choosing different g(t) pulse shapes and varying the parameters h and M.

## Slide 30: ARTM Tier 0 (PCM/FM) (CPFSK)
The way things were

## Slide 31: PCM/FM (Tier 0)
LPF
FM
Modulator
bipolar
NRZ-L
frequency is the time-derivative of the phase
since the phase is proportional to the integral of m(t), the frequency is proportional to m(t).
time-varying phase
Figure from " Quadrature Modulation for Aeronautical Telemetry”, by Michael Rice, BYU and Robert Jefferis, Tybrin Corp, ITC 2001. Reprinted by permission of the authors.

## Slide 32: Tier 0 in CPM Notation
M = 2 (binary)
i = 2di - 1
  di = {0, 1}, i = {-1, +1}
h = 0.7
g(t) is the normalized impulse response of a high order Bessel filter with 3 dB bandwidth = 0.7 * bit rate
  Normalized such that the integral over all time = 1/2
-< t <+

## Slide 33: PCM/FM as a Phase Modulation

## Slide 34: Power Spectral Density (PSD)

## Slide 35: Fractional Out-of-band Power
5 Mbps

## Slide 36: PCM/FM Summary
Legacy waveform
  Equipment is ubiquitous
Constant envelope
Several practical implementations
99.9% bandwidth: 2.03 times bit rate
M | i | h | g(t)
2 | {-1, +1} | 0.7 | Normalized impulse response of a high order Bessel filter with 3 dB bandwidth = 0.7 * bit rate

## Slide 37: ARTM Tier I (SOQPSK-TG)
The way things are

## Slide 38: Tier I Overview
Shaped OQPSK (SOQPSK)
  Constant envelope modulation(s) introduced by Hill (ITC 2000)
  Defined by 4 parameters ( r, B, T1, T2 )
  Compatible with existing efficient non-linear class C power amplifier
  Non-proprietary waveform
  Comparable in performance and interoperable with FQPSK
FQPSK
  Patented by K. Feher
  Defined by I and Q components
  Non-constant envelope
  Details are proprietary, contact Digcom

## Slide 39: SOQPSK in CPM Notation
M = 3 (ternary)
i = {-1, 0, +1}
  ai = 2di - 1
  ai = {-1, +1}, di = {0, 1}
h = 0.5
g(t) = windowed impulse response of spectral raised cosine
  Normalized such that the integral over all time = 1/2
-< t <+

## Slide 40: Definition of SOQPSK Pulse

## Slide 41: Frequency Pulse Shape, g(t)

## Slide 42: SOQPSK Variants
99.99% Bandwidth

## Slide 43: Optimal SOQPSK Variants
99.99% Bandwidth

## Slide 44: Unshaped Offset QPSK

## Slide 45: Slightly Shaped OQPSK

## Slide 46: MIL-STD SOQSPK

## Slide 47: SOQPSK-TG

## Slide 48: SOQPSK-TG
Jump to file://localhost/Users/TerryHill/Documents/Quasonix/TIMTER/SOQPSK Modulator10.xls

## Slide 49: SOQPSK-TG Phase Tree

## Slide 50: Power Spectral Density

## Slide 51: SOQPSK-TG Eye Patterns
Single-symbol detection is sub-optimal, but practical

## Slide 52: SOQPSK Constellations
Wait! I thought SOQPSK was constant envelope…

## Slide 53: Measured PSD (Tier 0 & 1)

## Slide 54: Fractional Out-of-band Power
5 Mbps
Often-cited factor of two

## Slide 55: Shaped Offset QPSK Summary
Constant envelope, CPM waveform
Adjustable shaping factor for BW and detection efficiency trade-off
Improved spectral containment over OQPSK
Compatible with standard OQPSK receivers and demodulators
Adopted as an ARTM Tier I waveform
99.9% bandwidth: 0.98 times bit rate
Interoperable with FQPSK
M | i | h | g(t)
3 | {-1, 0, +1} | 0.50 | Normalized windowed impulse response of a spectral raised cosine

## Slide 56: ARTM Tier II (ARTM CPM) (Multi-h CPM)
The way things can be

## Slide 57: Tier II Overview
Multi-h CPM characteristics
  Easy to trade off bandwidth and detection efficiency.
  Constant envelope is ideal for high efficiency non-linear power amplifiers.
  Detection efficiency is enhanced by periodically varying the modulation index (h).
    Extends the point at which competing paths remerge thereby increasing the minimum distance and decreasing the probability of symbol error.
  Nearly 2.5x improvement over PCM/FM in spectral efficiency with similar detection efficiency.

## Slide 58: ARTM Tier II in CPM Notation
M = 4 (quaternary)
i = 2 [2d1i + d0i] - 3
  i = {-3, -1, +1, +3}
  di = {0, 1}
h = {4/16, 5/16}, alternating
g(t) = raised cosine, 3 symbols (6 bits) in duration
  Normalized such that the integral over all time = 1/2
-< t <+

## Slide 59: Frequency Pulse & Phase Tree

## Slide 60: PSD (Tier 0, I, & II)

## Slide 61: Fractional Out-of-band Power
5 Mbps

## Slide 62: Tier II Multi-h CPM Summary
Similar detection efficiency to PCM/FM.
Constant envelope waveform is ideal for efficient non-linear PA’s.
Enhanced performance gained by increasing demodulator complexity.
99.9% bandwidth: 0.75 times bit rate
M | i | h | g(t)
4 | {-3, -1, +1, +3} | {4/16, 5/16} | Normalized raised cosine, 3 symbols (6 bits) long

## Slide 63: Side by Side Summary
Tier | M | i | h | g(t) | 99.9% BW
0 | 2 | {-1, +1} | 0.7 | Normalized impulse response of a high order Bessel filter with 3 dB bandwidth = 0.7 * bit rate | 2.03
I | 3 | {-1, 0, +1} | 0.5 | Normalized windowed impulse response of a spectral raised cosine, 8 bits long | 0.98
II | 4 | {-3, -1, +1, +3} | {4/16, 5/16} | Normalized raised cosine, 3 symbols (6 bits) long | 0.75

## Slide 64: Demodulation

## Slide 65: Demodulation
As the shop manual says, “Installation is reverse of removal.”
Demodulation is intrinsically more difficult
  Unknown carrier frequency
  Unknown carrier phase
  Unknown clock frequency and phase
  Signal corruption
    Noise
    Interference
    Multipath
    Doppler shift
Multiple techniques can be applied

## Slide 66: Single-Symbol Demodulation
Tier 0
  Legacy (nearly exclusive in 20th century)
  Simple to build
  Robust to signal defects and channel impairments
  ~3.5 to 5 dB short of theoretical limit
Tier I
  Requires optimization for SOQPSK
  Weakly synchronized
  Requires high SNR for acquisition
  ~1.0 to 1.5 dB short of theoretical limit
Tier II
  No practical single-symbol detectors

## Slide 67: Tier 0 Single-Symbol Detection
Differentiate the phase to get frequency
  Limiter-discriminator
  Phase locked loop
  Digital processing
If the frequency in this symbol > 0, data = 1
If the frequency in this symbol < 0, data = 0

## Slide 68: Tier 0 Frequency Detection

## Slide 69: SOQPSK-TG Eye Patterns
Single-symbol detection ignores memory inherent in waveform
Can be detected by conventional (non-shaped) offset QPSK demod
I&D detector endures additional loss due to waveform mismatch

## Slide 70: SOQPSK Constellations

## Slide 71: Waveform Comparison
PCM/FM (1x) SOQPSK (2x) Multi-h CPM (2.5x)

## Slide 72: Trellis Demodulation Overview
Tier 0
  Invented in 1974, introduced in 2001
    Osborne & Luntz, “Coherent and Noncoherent Detection of CPFSK”, IEEE T-COM, August 1974
  Requires significant signal processing power
  Signal defects and channel impairments require attention
    DSP techniques can be applied to solve these issues
  Operates within 0.2 dB of theoretical limit
Tier I
  Strong, rapid synchronization
  Operates within 0.2 dB of theoretical limit
Tier II
  Mandatory for practical implementation

## Slide 73: Tier 0 Phase Tree
h = 0.7
A multi-symbol detector finds the data sequence that best fits the observed phase trajectory

## Slide 74: Why Does It Matter?
If this bit is different, the phase trajectory is forever shifted…
Therefore, later bits can help make decisions about earlier bits.
Noise-corrupted trajectory
Single-symbol detector decides “zero”
Multi-symbol detector decides “one” – correcting the error

## Slide 75: Multi-Symbol Detector Example
Brute force approach – yields performance gain, but leads to extreme hardware complexity

## Slide 76: Generic Trellis Demodulator
Brains over brawn – Efficient computation yields the same performance as the brute force approach, with far less hardware

## Slide 77: Tier 0 BER Performance

## Slide 78: Legacy PCM/FM Transmitters
h = 0.6
h = 0.7
h = 0.8

## Slide 79: Effect of TX Deviation Error

## Slide 80: What About Phase Noise?
No phase noise:
The entire trellis is helpful
Minimal phase noise:
Several bits of the trellis are helpful
Significant phase noise:
A few bits of the trellis are helpful
Severe phase noise:
Not a candidate for trellis demodulation

## Slide 81: Phase Noise
Trellis demodulation is based on the assumption that the signal is following a predictable path through the trellis.
If this is not true (due to high phase noise), then a trellis demodulator may not provide the expected performance gain
Most often an issue at low bit rates
Some trellis demods handle this case by modifying the trellis calculations.

## Slide 82: SOQPSK Detection
Can be detected by conventional (non-shaped) offset QPSK demod
Non-matched filtering loss of about 2 dB
Butterworth lowpass filter is reasonable approximation to matched filter
Trellis detection is optimum, but more complex

## Slide 83: SOQPSK-TG Phase Tree

## Slide 84: SOQPSK Detection Efficiency
SOQPSK-TG

## Slide 85: Multi-h CPM Detection
Modulator intentionally creates severe inter-symbol interference
  3-symbol RC premod filter
Symbol-by-symbol detection is essentially useless
Trellis detection is required

## Slide 86: BER Performance Comparison

## Slide 87: Synchronization

## Slide 88: Telemetry Channels are Bursty
Figure from Robert Jefferis, Tybrin, Edwards AFB. Reprinted by permission of the author.
Synchronization is important!
In a typical flight test, the vast majority of bit errors occur at dropouts

## Slide 89: Synchronization Test
IRIG 118-12, Procedure 7.4 (Flat Fade Recovery Test)
Transmit randomized ones pattern
Measure time at which output becomes “all (or mostly) ones”
IRIG
Randomizer
Modulator
Add Noise
Noise
Switch
Demod
with
Derandomizer
Timer
Ones
Detector
All ones
Controller
Start
Stop

## Slide 90: Synchronization Parameters
Modulation technique
  Tier 0 uses more bandwidth – easier to synchronize to
  Tier I is spectrally compact, making it slippery – synchronization is more difficult
    Trellis demodulation helps achieve sync
  Tier II is even more compact – synchronization takes longer
Bit rate
  Fixed-duration tasks amount to more bits at high bit rates
Signal to noise ratio
  Sync times will be longer at low SNR
Synchronization threshold
  SNR at which the demodulator can acquire sync
Sync loss threshold
  SNR at which a synchronized demodulator will drop sync

## Slide 91: Tier 0 Synchronization, BER = 1e-5

## Slide 92: SOQPSK Synchronization, No Noise

## Slide 93: SOQPSK Synchronization, 6 dB

## Slide 94: SOQPSK Synchronization, 3 dB

## Slide 95: SOQPSK Synchronization, 1 dB

## Slide 96: SOQPSK Synchronization, -1 dB

## Slide 97: Synchronization Summary
The aeronautical telemetry channel is plagued with dropouts
Rapid synchronization, and synchronization at low SNR, is the best means of minimizing the impact of these dropouts
IRIG 118 defines test procedures for measuring sync time and sync thresholds
Pay attention to synchronization performance!

## Slide 98: Adjacent Channel Interference

## Slide 99: PSD is Half the Story
Overall spectral efficiency is determined by spacing between channels
Receiver selectivity affects channel spacing
A valid comparison must account for both transmitted spectrum and “tolerable” receiver filtering
Not all modulations are equally “tolerant” of IF filtering and interference
Multi-channel testing accounts for these factors

## Slide 100: Multi-channel ACI Test Set

## Slide 101: 9 Mbps Multi-h CPM, Multichannel

## Slide 102: BER as a Function of F
From Gene Law, “Recommended Minimum Telemetry Frequency Spacing With CPFSK, CPM, SOQPSK, and FQPSK Signals”, ITC 2003

## Slide 103: Degradation as a Function of F
From Gene Law, “Recommended Minimum Telemetry Frequency Spacing With CPFSK, CPM, SOQPSK, and FQPSK Signals”, ITC 2003

## Slide 104: ACI Summary
I/C=20 dB
From Gene Law, “Recommended Minimum Telemetry Frequency Spacing With CPFSK, CPM, SOQPSK, and FQPSK Signals”, ITC 2003

## Slide 105: Frequency Separation Rule
where:
  • ΔF0 = the minimum center frequency separation in MHz
  • Rs = bit rate of desired signal in Mb/s
  • Ri = bit rate of interfering signal in Mb/s
ΔF0 = as*Rs + ai*Ri
The NRZ PCM/FM signals are assumed to be premodulation filtered with a multi-pole filter with 3 dB point of 0.7 times the bit rate and the peak deviation is assumed to be approximately 0.35 times the bit rate.
The receiver IF filter is assumed to be no wider than 1.5 times the bit rate and provides at least 6 dB of attenuation of the interfering signal.
The interfering signal is assumed to be no more than 20 dB stronger than the desired signal.
The receiver is assumed to be operating in linear mode; no significant intermodulation products or spurious responses are present.

## Slide 106: Let’s Eat Students! Let’s Eat, Students!
Commas Save Lives
See you back here at _______ PM

## Slide 107: Multipath Propagation

## Slide 108: Multipath Propagation
Dry lake bed = smooth reflecting surface
Narrow beam receive antenna
Airborne transmitter
Line-of-sight communications link
Irregular terrain
Low elevation angle
Figure from Dr.Michael Rice, BYU Telemetry Laboratory, Provo, Utah. Reprinted by permission of the author.

## Slide 109: Multipath Experiments
127-PN
source
LPF
BPSK
mod
linear
PA
bipolar
NRZ @
10
Mbits
/sec
aircraft fuselage
hemispherically
omni
-directional
antenna
tracking antenna
wideband
telemetry
receiver
70 MHz IF
high speed
digital
oscilloscope
BPSK
demod
BER
analyzer
trigger
circuit
AGC
A/D
PC
GPS
sampling trigger
L-Band 1500 MHz
S-Band 2200 MHz
Figure from Dr.Michael Rice, BYU Telemetry Laboratory, Provo, Utah. Reprinted by permission of the author.

## Slide 110: Edwards AFB Flight Paths
Figure from Dr.Michael Rice, BYU Telemetry Laboratory, Provo, Utah. Reprinted by permission of the author.

## Slide 111: Signal Processing
-8
-6
-4
-2
0
2
4
6
8
1
2
3
4
5
6
7
8
9
10
Frequency (MHz), relative to carrier
S
x
(e
j
W
) (dB)
-8
-6
-4
-2
0
2
4
6
8
0
2
4
6
8
10
12
14
S
y
(e
j
W
) (dB)
Frequency (MHz), relative to carrier
-35
-30
-25
-20
-15
-10
-5
0
5
10
-8
-6
-4
-2
0
2
4
6
8
Frequency (MHz), relative to carrier
|H(e
j
W
)|
2
(dB)
Power spectral density of transmitted signal
Power spectral density of received signal
Estimate of channel transfer function
Figure from Dr.Michael Rice, BYU Telemetry Laboratory, Provo, Utah. Reprinted by permission of the author.

## Slide 112: Modeling Procedure
power spectral density of received signal
power spectral density of transmitted signal
Figure from Dr.Michael Rice, BYU Telemetry Laboratory, Provo, Utah. Reprinted by permission of the author.

## Slide 113: Measurement and Modeling
Figure from Dr.Michael Rice, BYU Telemetry Laboratory, Provo, Utah. Reprinted by permission of the author.

## Slide 114: Multipath on the Tarmac
Nearly static, frequency selective, long delays

## Slide 115: Multipath in Flight
Dynamic, frequency selective and flat fading, various delays

## Slide 116: Multipath During Flight
Frequency Diversity
Figure from Robert Jefferis, Tybrin, Edwards AFB. Reprinted by permission of the author.

## Slide 117: Classic Two-Ray Multipath
Figure from Robert Jefferis, Tybrin, Edwards AFB. Reprinted by permission of the author.

## Slide 118: Multipath Summary
If your test article operates near the ground, you are quite likely experiencing multipath.
If so, there will be intervals during which no useful data is recovered.
Loss of bit count integrity is likely
  Encrypted links will lose crypto sync
What to do?
Stay tuned for the “Mitigation” discussion

## Slide 119: DSP Techniques for Telemetry

## Slide 120: DSP Techniques for Telemetry
Maximal ratio combining – optimal against AWGN
  Polarization diversity
  Frequency diversity
  Receive-side processing, no transmitter impact
Adaptive equalization
  Powerful tool against multipath
  Receive-side processing, no transmitter impact
Best source selection
  Combats all forms of signal impairment
  Receive-side processing, no transmitter impact
Space-time coding (STC)
  Mitigates “built-in” multipath from dual TX antennas
  Requires dual transmitters
Forward error correction
  Spending bandwidth to buy link margin
  Requires encoder implemented in transmitter

## Slide 121: Maximal Ratio Combining
Many telemetry systems utilize diversity reception
  Frequency separation using two transmitter
  Orthogonal polarizations using cross-polarized antenna feeds
Combining two (or more) copies of the same signal
  Diversity combining
  Creates a third signal to be demodulated
  BER performance of third signal is better than either of the individual signals
Special case – the leading use of diversity
  Linearly polarized transmit antenna on test article – could be at any orientation
  Left-hand and right-hand circularly polarized receive antennas
  Each receive antenna loses half the transmit power
  Diversity combiner puts it all back together, eliminating the polarization loss
  Frequency diversity works the same way, but uses twice the bandwidth

## Slide 122: Maximal Ratio Combining
Weight each signal in proportion to its SNR and add
Yields optimum SNR on combined channel in AWGN
SNRcombined = SNRa + SNRb

## Slide 123: Maximal Ratio Combining
Jump to file://localhost/Users/TerryHill/Documents/Quasonix/ITC 2015/Diversity Combiner.avi

## Slide 124: BER Results - Fading Signals

## Slide 125: Measured Combiner BER - Tier 0

## Slide 126: Measured Combiner BER - Tier I

## Slide 127: Measured Combiner BER - Tier II

## Slide 128: Combiner Summary
Receive-side processing
  No transmitter impact
Phase aligns the signals
Forms weighted sum of two inputs
SNR of the weighted sum is at least as high as the better signal
May be as much as 3 dB higher (equal input case)
Conventional combiner design assumes signals are time-aligned
  Performance falls off rapidly with increasing time skew
  Combiner will probably fail altogether at ± ½ bit time skew
Some combiners do both phase alignment and time alignment
  Supports operation with spatially separated antennas
If you have access to two copies of the signal, use them!

## Slide 129: Adaptive Equalization

## Slide 130: Multipath is Ugly
Equalization can turn
this into… this.
Actual multipath from aircraft on the tarmac at Edwards AFB

## Slide 131: Adaptive Equalization
Consider the multipath channel to be a filter
  Varies over time
Consider building a filter which “undoes” the filtering imposed by the channel
  Let it keep track of the the channel and continuously adapt itself to the channel
Presto! You have an adaptive equalizer
  Can repair damage done by multipath
  Works with a single receiver
  Requires no bandwidth expansion
  Requires no changes to the transmitter

## Slide 132: Equalizer Techniques
J.G. Proakis, Digital Communications. 1989 2nd Edition

## Slide 133: Generic Adaptive Equalizer
Equalizer
Decision
Device
Equalizer
Adjustment
Error
Calculation
Training
Sequence
Symbol
Statistics
Training Mode
Blind Mode
Decision-Directed Mode
Transmitted Signal
Received Signal
Recovered
Data
Equalized
Signal
Error
Tap Weights
RF
Channel

## Slide 134: Equalizer AdaptationClick here

## Slide 135: Dial-a-Channel

## Slide 136: Adaptive Equalizer Summary
Adaptive equalizer can “undo” multipath distortion
Requires no changes at the transmit end
  If available, a training sequence can be helpful
Effectiveness of equalizer depends on the severity of the multipath
Well-designed equalizers monitor their own performance, and disengage when they are doing badly.
  This must be done without losing bit count integrity
If you have multipath, use an equalizer!

## Slide 137: Best Source Selection

## Slide 138: Combining Multiple Sources
Receive and demodulate the same signal at multiple receive sites
Funnel all the demodulated data to one central location
Time align the multiple data streams
Build a better output stream from the multiple input streams

## Slide 139: Selection Algorithms
Majority vote
  Reasonably effective with three or more sources
  Reduces to guesswork with only two sources
  Sub-optimal for any number of sources
PCM frame header accuracy
  Uses only a small fraction of the bits to make an estimate
  Poor resolution (BER is typically measured as Num_errors ÷ 32)
  Useless with encrypted data
Log-likelihood ratio
  Uses all the bits
  Works with encrypted data
  Max-likelihood (optimal) combining scheme
    Rice, Michael and Perrins, Erik. "Maximum Likelihood Detection From Multiple Bit Sources", Proceedings of the International Telemetering Conference, Las Vegas, NV, USA, 2015.

## Slide 140: Why Measure Data Quality?
Telemetry links suffer from a wide range of impairments
  Noise
  Interference
  Multipath
  Shadowing
  Loss of antenna track
We need a way to asses the impact of all these impairments
We need to compute pn
  Quickly
  Accurately
Rice, Michael and Perrins, Erik. "Maximum Likelihood Detection From Multiple Bit Sources", Proceedings of the International Telemetering Conference, Las Vegas, NV, USA, 2015.

## Slide 141: Terminology
BER (Bit Error Rate)
  Measured as (number of errors / number of bits)
  Assumes you know the data in advance
  Measuring very low BER requires a long time
  Converges to BEP if test runs long enough, and channel is static
BEP (Bit Error Probability)
  Calculated likelihood that a bit is in error
  Even very low BEP can be determined from only a few bits
DQM (Data Quality Metric)
  Derived directly from BEP
  Expressed as a 16-bit integer
DQE (Data Quality Encapsulation)
  Process of “bundling” DQM words and payload data
  Includes a sync word to aid BSS time alignment

## Slide 142: Data Quality Encapsulation
Payload data is bundled with its DQM, to give Best Source Selectors a valid basis for “best”
Interoperability among vendors requires standards
  DQM calibration against multiple signal impairments
  DQE packet structure
Quasonix has developed and shared an open DQM/DQE format
  Published at ITC 2015
  License-free, royalty-free
  Proposed for adoption as an RCC standard
Includes test procedures to evaluate DQM accuracy

## Slide 143: How to Assess Data Quality
Measured BER is not practical
  Requires known data in the stream – not possible with encryption
  Takes a long time to measure low BERs
Bit error probability (BEP), however…
  Does not require any known data
  Can be determined quickly and accurately from demodulator statistics
  Is an unbiased quality metric, regardless of channel impairments
  When calibrated per a standardized procedure, DQM based on BEP allows DQE from multiple vendors to interoperate
Each vendor can use their own algorithm for developing BEP
DQM is calculated directly from BEP
  Use of Likelihood Ratio leads to maximum likelihood BSS algorithms
  Converted to 16-bit integer on log scale

## Slide 144: Definition of DQM
Start with BEP, derived within demod
Likelihood Ratio (LR) = (1 - BEP) / BEP
DQM = min (round (log10 (LR) / 12 * (2^16)), 2^16 -1)
  16-bit unsigned integer, ranges from 0 to 65,535
Easily reversed:
  LR = 10^(-12 * DQM / 2^16)
  BEP = 1 / (1 + LR)
Define “Q” as the “User’s DQM”
  Q = 12 * DQM / 65535
  Represents the exponent of 10 in the BEP
  Examples:
    Q = 3  BEP = 1e-3
    Q = 7  BEP = 1e-7
  Arbitrarily cap Q at “a perfect 10”.
BEP | LR | DQM | Q
0.5 | 1.00 | 0 | 0.00
1E-01 | 1.11111E-01 | 5211 | 0.95
1E-02 | 1.01010E-02 | 10899 | 2.00
1E-03 | 1.00100E-03 | 16382 | 3.00
1E-04 | 1.00010E-04 | 21845 | 4.00
1E-05 | 1.00001E-05 | 27307 | 5.00
1E-06 | 1.00000E-06 | 32768 | 6.00
1E-07 | 1.00000E-07 | 38229 | 7.00
1E-08 | 1.00000E-08 | 43691 | 8.00
1E-09 | 1.00000E-09 | 49152 | 9.00
1E-10 | 1.00000E-10 | 54613 | 10.00
1E-11 | 1.00000E-11 | 60075 | 10.00
1E-12 | 1.00000E-12 | 65535 | 10.00

## Slide 145: DQE Format
Header
  16-bit sync pattern (0xFAC4)
    MSB first: 1111101011000100
  8-bit reserved word, potentially for packet header version number (currently 0)
  8-bit reserved word, potentially for source ID tag (currently 0)
  16-bit DQM
Payload data
  User selectable length, (128 ≤ N ≤ 16,536)
  Defaults to 4096
16-bit
Sync
Pattern
8-bit
Word
16-bit
DQM
N bits of payload data (128 ≤ N ≤ 16,536)
8-bit
Word

## Slide 146: DQM Parameter Trades
Choice of N impacts both DQM update rate and network efficiency

## Slide 147: Calibration of DQM
Calibrate DQM under various channel impairments:
  AWGN – static level
  AWGN – dynamic level (step response)
  Dropouts
  In-band and adjacent channel interference
  Phase noise
  Timing jitter
  Static multipath
Test procedures are being developed to evaluate accuracy of DQM
  Targeted for inclusion in IRIG 118

## Slide 148: DQM Calibration Fixture
Synthesize “impaired” RF signal
Recover the “corrupted” data (with clock)
Extract the frame sync word, including DQM
Measure BER of payload data
Compare DQM (converted to BEP) to measured BER
  Recorded and stored on a packet-by-packet basis

## Slide 149: DQM Calibration in AWGN
Required as a baseline for all other tests

## Slide 150: DQM Step Response
Assesses timeliness of DQM values
UUT stays synchronized during test
One block at each step is a blend of the two states

## Slide 151: DQM Fade Recovery
Includes UUT synchronization time

## Slide 152: DQM Interference Test
Interference is not AWGN, but it causes bit errors

## Slide 153: DQM in Multipath
Test run at high signal level – essentially no noise

## Slide 154: Does it work?
Four “poor” channels for input to BSS
One nearly error-free output from BSS
10-11
10-10
10-9
10-8
10-7
10-6
10-5
10-4
10-3
10-2
10-1
Inverted BER axis (up is good)

## Slide 155: BSS Summary
Correlating (time-aligning) source selectors deliver output data that is better than any single input stream
Combats all forms of signal impairment
  Noise
  Multipath
  Interference
  Shadowing
  Loss of antenna track
Diversity can be in any form
  Polarization
  Frequency
  Spatial
DQE / DQM equip the BSS to make optimal decisions

## Slide 156: Space-Time Coding

## Slide 157: Space-Time Coding
Polarization
receive diversity
Air vehicle maneuvering
masks Tx antenna and
causes polarization mismatch
Ground bounce
creates multipath
interference
Spatial transmit diversity
Ronald C. Crummett, Michael A. Jensen, Michael D. Rice
Department of Electrical and Computer Engineering
Brigham Young University

## Slide 158: Difficulties with TX Diversity
Antenna 2
Antenna 1
Spatially Separated Antennas Create
Interference Pattern

## Slide 159: MIMO Communications
MIMO: Multiple-Input Multiple-Output
Exploit multiple communication modes
H
Space-Time
Encoder
Data
Space-Time
Decoder
Data
Potential Benefits:
Diversity (robust communications)
Increased data throughput

## Slide 160: Alamouti Space-Time Coding
A B C D E F G H I J K L ...
space-time
encoder
A -B* C -D* E -F* G -H* I -J* K -L* ...
B A* D C* F E* H G* J I* L K* ...
traditional
1st block
2nd block
2 transmit antennas + 1 receive antenna version
2 transmit antennas + 2 receive antennas version
Calderbank showed that the Alamouti schemes are special cases of more general “orthogonal designs”

## Slide 161: Traditional Transmission
Each symbol is simultaneously sent from both antennas
Received signal energy
With the noise energy as No, the received SNR is
Power equally divided between antennas

## Slide 162: Alamouti Space-Time Coding
Signal energy over one symbol time:
Received noise energy:
Signal-to-Noise Ratio:

## Slide 163: Symbol Error Rate - QPSK
If the aircraft is rotated 360 in the horizontal plane
SER for QPSK in AWGN
Using two transmit antennas (traditional signaling)

## Slide 164: Symbol Error Rate - QPSK
For Alamouti signaling
Only magnitudes of
transfer functions
used in sum
Traditional signaling
Addition of transfer
functions leads to
reduction in effective
SNR

## Slide 165: Alamouti Scheme
Consider BPSK Signaling and Assume s1 = s2 = 1
Time Slot 1:
Gain Pattern:
Time Slot 2:
Gain Pattern:
Antenna Pattern Interpretation

## Slide 166: Symbol Error Rate
Similar expressions have been derived for:
Polarization diversity at receiver (Maximal Ratio combining)
One multipath (ground) bounce
BPSK and 16-QAM signal constellations
for both Traditional Signaling and Alamouti Signaling

## Slide 167: SER Simulations
Antenna Separation: 20’ Horizontal, 8’ Vertical
Antenna Patterns: Isotropic
Simple AWGN Channel

## Slide 168: SER Simulations
Results Identical to Single Receive Antenna System
Circular Polarization Diversity Reception

## Slide 169: Flight Tests: Airborne Configuration
10 W
10 W
STC
Transmitter
SOQPSK
Transmitter
L-band
isolator
+
+
÷
Channel Microwave
L320I
3 dB
3 dB
Pasternak
PE 7016-3
Narda 4322-2
upper antenna
lower antenna
10 W
5 W
5 W
5 W
5 W
SOQPSK
Transmitter
GPS/AHRS
house keeping link antenna
(separate lower antenna)
Quasonix
QSX-VLT-110-105-20-6A
Quasonix
Channel Microwave
L320I
L-band
isolator
Channel Microwave
L320I
L-band
isolator
Channel Microwave
L320I
L-band
isolator
Channel Microwave
L320I
Narda 4322-2
Narda 4322-2
L-band
isolator
Channel Microwave
L120I
Pasternak
PE 7016-3

## Slide 170: C-12 Beechcraft: Airborne Platform

## Slide 171: Antenna Locations

## Slide 172: Flight Tests: Idealized Gain Patterns
STC Frequency
Reference Link
Frequency

## Slide 173: Flight Tests: Ground Station Configuration
spectrum display
LNA
Bldg 4795: “Antenna 5”
EMT Model 150
5-m parabolic reflector
RHCP
multi-coupler
MU-Dell
2MDP1425
T/M
Receiver
1496.5 MHz
L-3/Microdyne
RCB 2000
Antenna Tracking
TCS ACU-M1
Housekeeping data
logging and display
A
20 dB
atten
1:4
split
MU-Dell
2MDA1424D-06
MU-Dell
2MDA1424D-06
unity gain input-to-each-output
PC
AGC
AM
Data
Clock
to antenna
servo motors
reference link
1514.5 MHz
STC link
1485.5 MHz
Spectrum
Analyzer
to DVD

## Slide 174: Test Flights: Ground Station Configuration
Clk
IF
70 MHz
Receiver
1514.5 MHz
M/A Com SMR 5550i
Tier 1
Demod.
RF Networks
Model 2120
BERT
Fireberd 6000A
Data
Receiver
1485.5 MHz
Microdyne 700 MR
AGC
AM
Data Acquisition
Wideband Systems
DRS 3300 (5 Msamples/s)
Clk
IF
70 MHz
Receiver
1485.5 MHz
M/A Com SMR 5550i
BYU
Prototype
STC Demod.
BERT
Fireberd 6000A
Data
to PC data logging
Receiver
1514.5 MHz
Microdyne 700 MR
AGC
AM
to PC data logging
Laptop PC
from splitter
National Instruments
DAQ (20 samples/s)
Data Acquisition
AGC
AGC

## Slide 175: Test Flights: Ground Station Configuration

## Slide 176: Test Flights: Ground Station Configuration

## Slide 177: STC Video Clip

## Slide 178: M1: Left-Hand Turn @ 10° bank

## Slide 179: M1: Test Results

## Slide 180: M2: Right-Hand Turn @ 10° bank

## Slide 181: M2: Test Results

## Slide 182: M3: Left-Hand Turn @ 30° bank

## Slide 183: M3: Test Results

## Slide 184: M4: Right-Hand Turn @ 30° bank

## Slide 185: M4: Test Results

## Slide 186: M3 to C2 Transition

## Slide 187: M3 to C2 Transition Test Results

## Slide 188: C2: Cords Road West-to-East

## Slide 189: C2: Test Results

## Slide 190: D2: Cords Road East-to-West

## Slide 191: D2: Test Results

## Slide 192: STC Summary
Dual-Antenna Diversity Scheme
Removes interference created by multiple transmit antennas
  SNR equivalent to single antenna transmission
  Multi-antenna scheme alleviates masking during maneuvering
  Can be used with diversity reception
Realtime hardware flight tested at Edwards AFB and showed substantial performance benefit

## Slide 193: Forward Error Correction

## Slide 194: Forward Error Correction
Basic premise
  Insert redundant bits into transmitted stream
  Use known relationships between bits to correct errors
Countless schemes have been developed
  Convolutional code / Viterbi decoder
  Block codes
    BCH
    Reed-Solomon
  Concatenated codes
    RS / Viterbi
    Turbo product codes (TPC)
  Low Density Parity Check (LDPC)

## Slide 195: LDPC Codes - History
LDPC: Low Density Parity Check
Linear block codes
  Some are systematic
Developed by Robert G. Gallager at M.I.T. in 1960
  Published by the M.I.T Press as a monograph in 1963
No practical implementations at that time
Re-discovered by David J.C. MacKay in 1996
  Began displacing turbo codes in the late 1990s
Recent history
  2003: LDPC code selected for the new DVB-S2 standard for the satellite digital TV
  2006: LDPC code selected for 10GBase-T Ethernet (10 Gbps over twisted-pair cables)
  2007: LDPC codes published by CCSDS as an “Orange Book”
  2008: LDPC code selected for the ITU-T G.hn standard
  2009: LDPC codes adopted for Wi-Fi 802.11 High Throughput (HT) PHY specification
  2012: LDPC code selected for integrated Network Enhanced Telemetry (iNET)

## Slide 196: LDPC AR4JA Codes
AR4JA: Accumulate-Repeat-4-Jagged-Accumulate
Published by CCSDS as an “Orange Book”
  Low Density Parity Check Codes For Use in Near-Earth and Deep Space Applications
Defines a family of systematic LDPC codes
Defines attached sync markers (ASM)
  Specified in section 6 of CCSDS Recommended Standard CCSDS 131.0-B-1
Present work based on the (6144, 4096) code

## Slide 197: Packet Assembly
Input 4096 data bits
  Randomize prior to encoding, if necessary
Compute and append 2048 parity bits
Prepend 256-bit attached sync marker (ASM)
  Yields a 6400-bit packet
  Each and every code word carries the ASM: A, A, Ā, A
    A = FCB88938D8D76A4F
    Ā = 034776C7272895B0
  Synchronization requires at most one code word
A
A
Ā
A
4096 Data Bits
2048 Parity bits

## Slide 198: Spectral Characterization

## Slide 199: Fractional Out-of-Band Power

## Slide 200: Decoder
Demodulate SOQPSK with soft decisions
  Implemented 8-bit decisions
    Iterative decoders work best with high resolution soft decisions
  Estimate Eb/N0 for soft decision scaling
Correlate for ASM with hard decisions
  Resolves the 4-ary phase ambiguity in SOQPSK
  Virtually certain sync at Eb/N0 = 0 dB
Initialize decoder
Execute decode iterations until next code word
  Coding gain varies with bit rate

## Slide 201: Measured BER Results

## Slide 202: LDPC from Appendix 2-D

## Slide 203: BER – All Modes

## Slide 204: Conclusions
Rate 2/3 LDPC code yields ≈9 dB coding gain relative to uncoded SOQPSK
  ±0.5 dB, depending on data rate
256-bit ASM provides reliable, fast synchronization at Eb/N0 < 0 dB
  Synchronization is consistently achieved in < 4096 data bits
Bandwidth expansion of 25/16
  Still 22% less bandwidth than legacy PCM/FM
SOQPSK with LDPC offers a reasonable trade of spectral efficiency for a significant gain in detection efficiency
5 other LDPC codes offer similar trade of bandwidth for BER performance

## Slide 205: How Well Does It All Work Together?
Yuma Proving Grounds, AZ
Feb 8-11, 2016

## Slide 206: Recipe for Delivering Every Bit
Space Time Coding (STC)
  Eliminates aircraft pattern nulls
Low Density Parity Check (LDPC) coding
  Improves margin, stops “dribbling errors”
Adaptive Equalization (for non-STC signals)
  Mitigates multipath
Spatial diversity with correlating source selection
  Eliminate coverage-based dropouts
  Requires DQE/DQM for optimal operation
  TMoIP makes delivery easy

## Slide 207: Multiple Receiving Sites
Best Source Selector used 6 inputs: Ch1, Ch2 from each source, but not the combiner outputs (not enough channels).

## Slide 208: Dual Transmitter – S band – 10 W each output
Installed in UH-1 (Huey) helicopter with top and bottom blade antennas

## Slide 209: YPG Test Sites
Site CM4
Site 2
Site 4
Site 4 to Site CM4 = 14.25 mi
Laguna Airfield

## Slide 210: Analysis using Data Logs
Ch1, Ch2
DQE
Ch1, Ch2
DQE
Ch1, Ch2
DQE
Site 4
‘Best’
F1
Ch1
Ch2
F2
Site 2
F1
Ch1
Ch2
F2
CM4
F1
Ch1
Ch2
F2
F1
Top
Antenna
F2
Bottom
Antenna
Transmit F1-Top, F2-Bottom
3 Receive Sites
6 Clock & Data streams provided to A-CSS with Data Quality Encapsulation (DQE)
DQE = Receiver inserts periodic estimate of instantaneous BEP
Items of interest
  Top vs Bottom Antenna
  Individual Site Performance
  Source Selector Performance
Receiver Analyzer
BERT Log
Receiver Analyzer Log
(BER of A-CSS output)
A-CSS Log
(BEP of each time-aligned source)
Data Log on
Each Receiver
(BEP, BER, RSSI,...)

## Slide 211: Flight 1 – PCM/FM 5 Mbps Link Availability Summary (PN23 BER)

## Slide 212: Flight 2 – SOQPSK 5 Mbps Link Availability Summary (PN23 BER)

## Slide 213: Flight 3 – SOQPSK 20 Mbps Link Availability Summary (PN23 BER)

## Slide 214: Flight 4 – STC/LDPC 5 Mbps Link Availability Summary (PN23 BER)

## Slide 215: The elusive zero-error link…..
STC/LDPC from 3 sites at 5 MBPS
1st pass PN23 -- 34 minutes of helicopter flight across YPG…
Error-free!
2nd pass video with no freeze ups or blackouts!

## Slide 216: Performance Comparison and Summary

## Slide 217: Power Spectral Densities

## Slide 218: Out-of-Band Power

## Slide 219: BER Performance Comparison

## Slide 220: Bandwidth-Power Plane

## Slide 221: Acknowledgements
Mark Geoghegan, Quasonix
Dr. Michael Rice, Brigham Young University
Bob Jefferis, Tybrin, Edwards AFB
Kip Temple, ARTM, Edwards AFB
Gene Law, NAWCWD, Pt. Mugu
Vickie Reynolds, White Sands Missile Range

## Slide 222: Questions/Comments