## Slide 1: Advanced Modulation Techniques for Telemetry
A Short Course at the
International Telemetering Conference
Terry Hill, Quasonix
Glendale, AZ • October 26, 2026

## Slide 2: Course Outline
01 | Performance Metrics
02 | Continuous Phase Modulation (CPM) Tier 0 Tier I Stier II
03 | 16-APSK
04 | Demodulation Synchronization
05 | Channel Impairments Adjacent Channel Interference Multipath Propagation
06 | Impairment Mitigation Techniques Diversity Combining Lunch DQE/DQM Adaptive Equalization Best Channel Selection Best Source Selection Space-Time Coding Forward Error Correction (FEC)
07 | Using All the Tools Together
08 | Performance Comparison & Summary

## Slide 3: Performance Metrics
Bandwidth Efficiency
Bandwidth-Power plane
Information Fidelity
How many of the bits are correct?
How much (or how little) spectrum do I need?

## Slide 4: Bandwidth Efficiency
Power spectral density
Function of transmitter only
Fractional Out-of-band Power
Channel spacing with adjacent channel interference
Function of transmitter and receiver
We’ll review this in depth later
DD1494
Spectrum manager’s vantage point

## Slide 5: Power Spectral Density (PSD)

## Slide 6: Fractional Out-of-band Power
5 Mbps

## Slide 7: DD1494
5 Mbps

## Slide 8: DD1494 Calculator
5 Mbps

## Slide 9: DD1494 Guides
Handbook: Additional data to support spectrum certification requests for aeronautical mobile telemetry systems
Handbook: Telemetry systems radio frequency

## Slide 10: Information Fidelity
Additive White Gaussian Noise (AWGN) channels
Data Quality Metric (DQM)
Come back after lunch!
Bursty (dropout) channels
Cumulative error count
Link Availability
  Percent of the 1-second intervals that the BER is less than 10-5
Bit Error Probability (BEP) or Bit Error Rate (BER)

## Slide 11: BER Performance Comparison

## Slide 12: Today’s Modulation Tour
16-APSK

## Slide 13: Continuous Phase Modulation

## Slide 14: The Modulation Universe
Analog, Digital
Amplitude modulation
Quadrature amplitude modulation
Angle modulations
  Frequency modulation
  Phase modulation
Amplitude/Phase Shift Keying (APSK)

## Slide 15: Angle Modulations
Includes both frequency modulation and phase modulation
Some have an amplitude modulation component
  BPSK
  QPSK
  Offset QPSK
Some are constant envelope
  Binary FM
    FSK, MSK, premod filtered MSK, GMSK
  M-ary FSK
  SOQPSK
  Multi-h continuous phase modulation
  No amplitude variation
Saturated power amplifiers are ideal for constant envelope waveforms

## Slide 16: Saturated Power Amplifiers
DC-to-RF conversion efficiency is important
  Minimizes cooling requirements
  Maximizes battery life
Maximizing efficiency demands nonlinear operation
Non-linear operation creates AM-AM and AM-PM conversion:

## Slide 17: Constant Envelope Modulations
Before ARTM (Tier 0)
  PCM/FM
  “Legacy” waveform for telemetry
Advanced Range Telemetry (ARTM) Program
  ARTM Tier 1
    Proprietary Feher-patented FQPSK
      FQPSK-B, Revision A1
      FQPSK-JR
    SOQPSK-TG
      Equivalent in performance to FQPSK
      Non-proprietary
ARTM Tier 2
    Multi-h CPM (M=4, L=3RC, h1 = 4/16, h2 = 5/16)
PCM/FM, SOQPSK and Multi-h CPM are all continuous phase modulations (CPM)

## Slide 18: CPM Notation and Parameters
Where i represents an M-ary symbol sequence
  i derived from input bits di
h is the modulation index
g(t) is the frequency pulse shape in the interval 0 < t < LT
  L = 1 is “full response” signaling
  L > 1 yields “partial response”
CPM is a modulation with memory due to the constraint of continuous phase. Further memory is introduced with L > 1.
-< t <+

## Slide 19: CPM Characteristics
Continuous Phase
Constant envelope
Signals are described by their phase trajectories
  Phase tree representation is complete
PSD and BER can be “traded” by
  Varying h, modulation index
  Changing g(t), the frequency pulse shape
Phase trellis decoder is optimum for any variant of CPM

## Slide 20: Phase Tree Representation

## Slide 21: M=2, h=1/2, 1REC (MSK)
PSD vertical axis is dBc per FFT bin
1 FFT bin = 1/64 * symbol rate

## Slide 22: M=4, h=1/4, 1REC
PSD vertical axis is dBc per FFT bin
1 FFT bin = 1/64 * symbol rate

## Slide 23: M=4, h=1/4, 1RC
PSD vertical axis is dBc per FFT bin
1 FFT bin = 1/64 * symbol rate

## Slide 24: M=4, h=1/4, 2RC
PSD vertical axis is dBc per FFT bin
1 FFT bin = 1/64 * symbol rate

## Slide 25: M=4, h=1/4, 3RC
PSD vertical axis is dBc per FFT bin
1 FFT bin = 1/64 * symbol rate

## Slide 26: Multi-h CPM
Cyclically rotates through multiple “sets” of FSK tones
Increases minimum distance in trellis
  Improves BER performance
Widely proposed for high-performance nonlinear channels
  MIL-STD-188-181B

## Slide 27: M=2, h1=1/4, h2=1/2, 1REC
PSD vertical axis is dBc per FFT bin
1 FFT bin = 1/64 * symbol rate

## Slide 28: M=4, h1=4/16, h2=5/16, 3RC
PSD vertical axis is dBc per FFT bin
1 FFT bin = 1/64 * symbol rate
ARTM Tier II Waveform

## Slide 29: CPM Summary
To reduce bandwidth of a CPM signal, the phase transitions must be smoothed by:
  Requiring phase to have more continuous derivatives
  Spreading the phase change over more intervals (i.e., L > 1)
  Reducing h
The shape of g(t) determines the smoothness of the information-carrying phase
An endless variety of CPM schemes can be obtained by choosing different g(t) pulse shapes and varying the parameters h and M.

## Slide 30: ARTM Tier 0 (PCM/FM) (CPFSK)
The way things were

## Slide 31: PCM/FM (Tier 0)
LPF
FM
Modulator
bipolar
NRZ-L
frequency is the time-derivative of the phase
since the phase is proportional to the integral of m(t), the frequency is proportional to m(t).
time-varying phase
Figure from " Quadrature Modulation for Aeronautical Telemetry”, by Michael Rice, BYU and Robert Jefferis, Tybrin Corp, ITC 2001. Reprinted by permission of the authors.

## Slide 32: Tier 0 in CPM Notation
-< t <+
M = 2 (binary)
i = 2di - 1
  di = {0, 1}, i = {-1, +1}
h = 0.7
g(t) is the normalized impulse response of a high order Bessel filter with 3 dB bandwidth = 0.7 * bit rate
  Normalized such that the integral over all time = 1/2

## Slide 33: PCM/FM as a Phase Modulation

## Slide 34: Power Spectral Density (PSD)

## Slide 35: Fractional Out-of-band Power
5 Mbps

## Slide 36: PCM/FM Summary
Legacy waveform
  Equipment is ubiquitous
Constant envelope
Several practical implementations
99.9% bandwidth: 2.03 times bit rate
M | i | h | g(t)
2 | {-1, +1} | 0.7 | Normalized impulse response of a high order Bessel filter with 3 dB bandwidth = 0.7 * bit rate

## Slide 37: ARTM Tier I (SOQPSK-TG)
The way things are

## Slide 38: Tier I Overview
FQPSK
Patented by K. Feher
Defined by I and Q components
Non-constant envelope
Details are proprietary, contact Digcom
Shaped OQPSK (SOQPSK)
Constant envelope modulation(s) introduced by Hill (ITC 2000)
Defined by 4 parameters ( r, B, T1, T2 )
Compatible with existing efficient non-linear class C power amplifier
Non-proprietary waveform
Comparable in performance and interoperable with FQPSK

## Slide 39: SOQPSK in CPM Notation
M = 3 (ternary)
i = {-1, 0, +1}
  ai = 2di - 1
  ai = {-1, +1}, di = {0, 1}
-< t <+
h = 0.5
g(t) = windowed impulse response of spectral raised cosine
  Normalized such that the integral over all time = 1/2

## Slide 40: Definition of SOQPSK Pulse

## Slide 41: Frequency Pulse Shape, g(t)
Parameter | SOQPSK-A | SOQPSK-B
ρ | 1.0 | 0.5
B | 1.35 | 1.45
T1 | 1.4 | 2.8
T2 | 0.6 | 1.2

## Slide 42: SOQPSK Variants
99.99% Bandwidth

## Slide 43: Optimal SOQPSK Variants
99.99% Bandwidth

## Slide 44: Unshaped Offset QPSK

## Slide 45: Slightly Shaped OQPSK

## Slide 46: MIL-STD SOQSPK

## Slide 47: SOQPSK-TG

## Slide 48: SOQPSK-TG Phase Tree

## Slide 49: Power Spectral Density

## Slide 50: SOQPSK-TG Eye Patterns
Single-symbol detection is sub-optimal, but practical

## Slide 51: SOQPSK Constellations
Wait! I thought SOQPSK was constant envelope…

## Slide 52: Measured PSD (Tier 0 & 1)

## Slide 53: Fractional Out-of-band Power
5 Mbps
Often-cited factor of two

## Slide 54: Shaped Offset QPSK Summary
Constant envelope, CPM waveform
Adjustable shaping factor for BW and detection efficiency trade-off
Improved spectral containment over OQPSK
Compatible with standard OQPSK receivers and demodulators
Adopted as an ARTM Tier I waveform
99.9% bandwidth: 0.98 times bit rate
Interoperable with FQPSK
M | i | h | g(t)
3 | {-1, 0, +1} | 0.50 | Normalized windowed impulse response of a spectral raised cosine

## Slide 55: ARTM Tier II (ARTM CPM) (Multi-h CPM)
The way things can be

## Slide 56: Tier II Overview
Multi-h CPM characteristics
Easy to trade off bandwidth and detection efficiency.
Constant envelope is ideal for high efficiency non-linear power amplifiers.
Detection efficiency is enhanced by periodically varying the modulation index (h).
  Extends the point at which competing paths remerge thereby increasing the minimum distance and decreasing the probability of symbol error.
Nearly 2.5x improvement over PCM/FM in spectral efficiency with similar detection efficiency.

## Slide 57: ARTM Tier II in CPM Notation
-< t <+
M = 4 (quaternary)
i = 2 [2d1i + d0i] - 3
  i = {-3, -1, +1, +3}
  di = {0, 1}
h = {4/16, 5/16}, alternating
g(t) = raised cosine, 3 symbols (6 bits) in duration
  Normalized such that the integral over all time = 1/2

## Slide 58: Frequency Pulse & Phase Tree

## Slide 59: PSD (Tier 0, I, & II)

## Slide 60: Fractional Out-of-band Power
5 Mbps

## Slide 61: Tier II Multi-h CPM Summary
Similar detection efficiency to PCM/FM.
Constant envelope waveform is ideal for efficient non-linear PA’s.
Enhanced performance gained by increasing demodulator complexity.
99.9% bandwidth: 0.75 times bit rate
M | i | h | g(t)
4 | {-3, -1, +1, +3} | {4/16, 5/16} | Normalized raised cosine, 3 symbols (6 bits) long

## Slide 62: Side by Side Summary
Tier | M | i | h | g(t) | 99.9% BW
0 | 2 | {-1, +1} | 0.7 | Normalized impulse response of a high order Bessel filter with 3 dB bandwidth = 0.7 * bit rate | 2.03
I | 3 | {-1, 0, +1} | 0.5 | Normalized windowed impulse response of a spectral raised cosine, 8 bits long | 0.98
II | 4 | {-3, -1, +1, +3} | {4/16, 5/16} | Normalized raised cosine, 3 symbols (6 bits) long | 0.75

## Slide 63: Amplitude/Phase Shift Keying (APSK)
Things to come?

## Slide 64: 16-APSK Constellation - Ideal

## Slide 65: 16-APSK Spectrum - Ideal

## Slide 66: 16-APSK Transmitter

## Slide 67: 16-APSK TX Output

## Slide 68: 16-APSK BER

## Slide 69: 16-APSK Spectrum @ 1 Watt

## Slide 70: 16-APSK Spectrum @ 6 Watts

## Slide 71: 16-APSK Conclusions
Smart people are working hard
The circuits need work
More to come!
The math is willing

## Slide 72: Demodulation
Short Break

## Slide 73: Demodulation
As the shop manual says, “Installation is reverse of removal.”
Demodulation is intrinsically more difficult
  Unknown carrier frequency
  Unknown carrier phase
  Unknown clock frequency and phase
  Signal corruption
    Noise
    Interference
    Multipath
    Doppler shift
Multiple techniques can be applied

## Slide 74: Single-Symbol Demodulation
Tier 0
Tier II
No practical single-symbol detectors
Tier I
Requires optimization for SOQPSK
Weakly synchronized
Requires high SNR for acquisition
~1.0 to 1.5 dB short of theoretical limit
Simple to build
Robust to signal defects and channel impairments
~3.5 to 5 dB short of theoretical limit

## Slide 75: Tier 0 Single-Symbol Detection
Differentiate the phase to get frequency
  Limiter-discriminator
  Phase locked loop
  Digital processing
If the frequency in this symbol > 0, data = 1
If the frequency in this symbol < 0, data = 0

## Slide 76: Tier 0 Frequency Detection

## Slide 77: SOQPSK-TG Eye Patterns
Single-symbol detection ignores memory inherent in waveform
Can be detected by conventional (non-shaped) offset QPSK demod
I&D detector endures additional loss due to waveform mismatch

## Slide 78: SOQPSK Constellations

## Slide 79: Waveform Comparison
PCM/FM (1x)
SOQPSK (2x)
Multi-h CPM (2.5x)

## Slide 80: Trellis Demodulation Overview
Tier 0
Tier II
Mandatory for practical implementation
Tier I
Strong, rapid synchronization
Operates within 0.2 dB of theoretical limit
Invented in 1974, introduced in 2001
  Osborne & Luntz, “Coherent and Noncoherent Detection of CPFSK”, IEEE T-COM, August 1974
Requires significant signal processing power
Signal defects and channel impairments require attention
  DSP techniques can be applied to solve these issues
Operates within 0.2 dB of theoretical limit

## Slide 81: Tier 0 Phase Tree
h = 0.7
A multi-symbol detector finds the data sequence that best fits the observed phase trajectory

## Slide 82: Why Does It Matter?
If this bit is different, the phase trajectory is forever shifted…
Therefore, later bits can help make decisions about earlier bits.
Noise-corrupted trajectory
Single-symbol detector decides “zero”
Multi-symbol detector decides “one” – correcting the error

## Slide 83: Multi-Symbol Detector Example
Brute force approach – yields performance gain, but leads to extreme hardware complexity

## Slide 84: Generic Trellis Demodulator
Brains over brawn – Efficient computation yields the same performance as the brute force approach, with far less hardware

## Slide 85: Tier 0 BER Performance

## Slide 86: Legacy PCM/FM Transmitters
h = 0.6
h = 0.7
h = 0.8

## Slide 87: Effect of TX Deviation Error

## Slide 88: What About Phase Noise?
No phase noise:
The entire trellis is helpful
Significant phase noise:
A few bits of the trellis are helpful
Minimal phase noise:
Several bits of the trellis are helpful
Severe phase noise:
Not a candidate for trellis demodulation

## Slide 89: Phase Noise
Trellis demodulation is based on the assumption that the signal is following a predictable path through the trellis.
If this is not true (due to high phase noise), then a trellis demodulator may not provide the expected performance gain
Most often an issue at low bit rates
Some trellis demods handle this case by modifying the trellis calculations.

## Slide 90: SOQPSK Detection
Can be detected by conventional (non-shaped) offset QPSK demod
Non-matched filtering loss of about 2 dB
Butterworth lowpass filter is reasonable approximation to matched filter
Trellis detection is optimum, but more complex

## Slide 91: SOQPSK-TG Phase Tree

## Slide 92: SOQPSK Detection Efficiency
SOQPSK-TG

## Slide 93: Multi-h CPM Detection
Trellis detection is required
Symbol-by-symbol detection is essentially useless
Modulator intentionally creates severe inter-symbol interference
3-symbol RC premod filter

## Slide 94: BER Performance Comparison

## Slide 95: Synchronization

## Slide 96: Telemetry Channels are Bursty
Synchronization is important!
Figure from Robert Jefferis, Tybrin, Edwards AFB. Reprinted by permission of the author.
In a typical flight test, the vast majority of bit errors occur at dropouts

## Slide 97: Synchronization Test
IRIG
Randomizer
Modulator
Add Noise
Noise
Switch
Demod
with
Derandomizer
Timer
Ones
Detector
All ones
Controller
Start
Stop
IRIG 118-12, Procedure 7.4 (Flat Fade Recovery Test)
Transmit randomized ones pattern
Measure time at which output becomes “all (or mostly) ones”

## Slide 98: Synchronization Parameters
Signal to noise ratio
Sync times will be longer at low SNR
Synchronization threshold
SNR at which the demodulator can acquire sync
Sync loss threshold
SNR at which a synchronized demodulator will drop sync
Modulation technique
Tier 0 uses more bandwidth – easier to synchronize to
Tier I is spectrally compact, making it slippery – synchronization is more difficult
  Trellis demodulation helps achieve sync
Tier II is even more compact – synchronization takes longer
Bit rate
Fixed-duration tasks amount to more bits at high bit rates

## Slide 99: Tier 0 Synchronization, BER = 1e-5

## Slide 100: SOQPSK Synchronization, No Noise

## Slide 101: SOQPSK Synchronization, 6 dB

## Slide 102: SOQPSK Synchronization, 3 dB

## Slide 103: SOQPSK Synchronization, 1 dB

## Slide 104: SOQPSK Synchronization, -1 dB

## Slide 105: Synchronization Summary
IRIG 118 defines test procedures for measuring sync time and sync thresholds
Rapid synchronization, and synchronization at low SNR, is the best means of minimizing the impact of these dropouts
Pay attention to synchronization performance!
The aeronautical telemetry channel is plagued with dropouts

## Slide 106: Adjacent Channel Interference

## Slide 107: PSD is Half the Story
Overall spectral efficiency is determined by spacing between channels
Receiver selectivity affects channel spacing
A valid comparison must account for both transmitted spectrum and “tolerable” receiver filtering
Not all modulations are equally “tolerant” of IF filtering and interference
Multi-channel testing accounts for these factors

## Slide 108: Multi-channel ACI Test Set

## Slide 109: 9 Mbps Multi-h CPM, Multichannel

## Slide 110: BER as a Function of F
From Gene Law, “Recommended Minimum Telemetry Frequency Spacing With CPFSK, CPM, SOQPSK, and FQPSK Signals”, ITC 2003

## Slide 111: Degradation as a Function of F
From Gene Law, “Recommended Minimum Telemetry Frequency Spacing With CPFSK, CPM, SOQPSK, and FQPSK Signals”, ITC 2003

## Slide 112: ACI Summary
I/C=20 dB
From Gene Law, “Recommended Minimum Telemetry Frequency Spacing With CPFSK, CPM, SOQPSK, and FQPSK Signals”, ITC 2003

## Slide 113: Frequency Separation Rule
The NRZ PCM/FM signals are assumed to be premodulation filtered with a multi-pole filter with 3 dB point of 0.7 times the bit rate and the peak deviation is assumed to be approximately 0.35 times the bit rate.
The receiver IF filter is assumed to be no wider than 1.5 times the bit rate and provides at least 6 dB of attenuation of the interfering signal.
The interfering signal is assumed to be no more than 20 dB stronger than the desired signal.
The receiver is assumed to be operating in linear mode; no significant intermodulation products or spurious responses are present.
where:
  • ΔF0 = the minimum center frequency separation in MHz
  • Rs = bit rate of desired signal in Mb/s
  • Ri = bit rate of interfering signal in Mb/s
ΔF0 = as*Rs + ai*Ri
Modulation Type | as |  | ai | Rs + Ri
NRZ PCM/FM | 1 | For receivers with RLC final Intermediate Frequency (IF) filters | 1.2 | 2.2
 | 0.7 | For receivers with Surface Acoustic Wave (SAW) or digital IF filters | 1.2 | 1.9
 | 0.5 | With multi-symbol detectors (or equivalent devices) | 1.2 | 1.7
FQPSK-B, FQPSK-JR, SOQPSK-TG | 0.45 |  | 0.65 | 1.1
ARTM CPM | 0.35 |  | 0.5 | 0.85

## Slide 114: Multipath Propagation
Brace yourself!
Greek symbols ahead!

## Slide 115: Multipath Propagation
Dry lake bed = smooth reflecting surface
Narrow beam receive antenna
Airborne transmitter
Line-of-sight communications link
Irregular terrain
Low elevation angle
Figure from Dr.Michael Rice, BYU Telemetry Laboratory, Provo, Utah. Reprinted by permission of the author.

## Slide 116: Assumptions
Line-of-sight propagation path
L-1 multipath propagation paths
Figure from Dr.Michael Rice, BYU Telemetry Laboratory, Provo, Utah. Reprinted by permission of the author.
Complex-valued path loss
Channel can be modeled as a linear time-invariant (LTI) system over “short enough” time interval

## Slide 117: 2-Ray Transfer Function
Magnitude of first multipath reflection: G1
“sweep rate” of multipath null ~
(dB)
1 (0 dB)
Figure from Dr.Michael Rice, BYU Telemetry Laboratory, Provo, Utah. Reprinted by permission of the author.

## Slide 118: 3-Ray Transfer Function
1 (0 dB)
M
D
(dB)
(3-Ray Model)
(dB)
(2-Ray Model)
Figure from Dr.Michael Rice, BYU Telemetry Laboratory, Provo, Utah. Reprinted by permission of the author.

## Slide 119: Multipath on the Tarmac
Nearly static, frequency selective, long delays

## Slide 120: Multipath in Flight
Dynamic, frequency selective and flat fading, various delays

## Slide 121: Multipath Summary
If your test article operates near the ground, you are quite likely experiencing multipath.
If so, there will be intervals during which no useful data is recovered.
Loss of bit count integrity is likely
  Encrypted links will lose crypto sync
What to do?
Stay tuned for the “Adaptive Equalizer” discussion

## Slide 122: DSP Techniques for Telemetry

## Slide 123: Receiver-Only DSP Techniques
Adaptive equalization
Powerful tool against multipath
Best channel selection
Handles the “non-combinable” cases
Best source selection
Combats all forms of signal impairment
Receive-side processing, no transmitter impact
Maximal ratio combining – optimal against AWGN
Polarization diversity
Frequency diversity
Data Quality Metric (DQM) / Data Quality Encapsulation (DQE)
IRIG 118-22, Chapter 11

## Slide 124: Diversity Combining

## Slide 125: Maximal Ratio Combining
Many telemetry systems utilize diversity reception
Frequency separation using two transmitter
Orthogonal polarizations using cross-polarized antenna feeds
Combining two (or more) copies of the same signal
Diversity combining
Creates a third signal to be demodulated
BER performance of third signal is better than either of the individual signals
Special case – the leading use of diversity
Linearly polarized transmit antenna on test article – could be at any orientation
Left-hand and right-hand circularly polarized receive antennas
Each receive antenna loses half the transmit power
Diversity combiner puts it all back together, eliminating the polarization loss
Frequency diversity works the same way, but uses twice the bandwidth

## Slide 126: Maximal Ratio Combining
Weight each signal in proportion to its SNR and add
Yields optimum SNR on combined channel in AWGN
SNRcombined = SNRa + SNRb

## Slide 127: Maximal Ratio Combining

## Slide 128: BER Results - Fading Signals

## Slide 129: Measured Combiner BER - Tier 0

## Slide 130: Measured Combiner BER - Tier I

## Slide 131: Measured Combiner BER - Tier II

## Slide 132: Combiner Summary
Conventional combiner design assumes signals are time-aligned
  Performance falls off rapidly with increasing time skew
  Combiner will probably fail altogether at ± ½ bit time skew
Some combiners do both phase alignment and time alignment
  Supports operation with spatially separated antennas
If you have access to two copies of the signal, use them!
Receive-side processing
  No transmitter impact
Phase aligns the signals
Forms weighted sum of two inputs
SNR of the weighted sum is at least as high as the better signal
May be as much as 3 dB higher (equal input case)

## Slide 133: Let’s Eat Students! Let’s Eat, Students!
Commas Save Lives
See you back here at _______ PM

## Slide 134: Data Quality Metric (DQM)

## Slide 135: DQE/DQM Evolution
Milestones | Contributions
2015 Hill ITC Paper - “Metrics and Test Procedures for Data Quality Estimation in the Aeronautical Telemetry Channel” | DQE/DQM transport protocol to support efficient multiple source TM combining
2015 Rice/Perrins ITC Paper -“Maximum Likelihood Detection from Multiple Bit Sources” | Optimal combining recipe and performance analysis - Maximum Likelihood Bit Detection (MLBD)
IRIG 106-22 Chapter 2, Appendix 2-G - “Standards for Data Quality Metrics and Data Quality Encapsulation” | Standardized in IRIG 106-22
2022 Temple ITC Paper - “Some Thoughts on Testing the Data Quality Metric” | Proposed DQE/DQM verification test methods
IRIG 118-22 Release 2 Volume 2., Chapter 11, 2022 -“Test procedures for assessing telemetry receiver data quality metrics” | DQE/DQM verification test methods standardized in IRIG 118-22
Industry Day on DQE/DQM assessment 10/28/22 | Initial multi-vendor DQE/DQM performance/compatibility testing
2023 Geoghegan ITC Paper -“Data Quality Metric (DQM) – How accurate does it need to be?” | Determined relationship between worst case system MLBD performance loss and DQM estimation error
*** Industry Day 2 on DQE/DQM assessment 10/25/24 *** | Multi-vendor DQE/DQM performance/compatibility testing (all tests with real-time results)

## Slide 136: How to Assess Data Quality
Each vendor can use their own algorithm for developing BEP
DQM is calculated directly from BEP
Use of Likelihood Ratio leads to maximum likelihood BSS algorithms
Converted to 16-bit integer on log scale
Measured BER is not practical
Requires known data in the stream – not possible with encryption
Takes a long time to measure low BERs
Bit error probability (BEP), however…
Does not require any known data
Can be determined quickly and accurately from demodulator statistics
Is an unbiased quality metric, regardless of channel impairments
When calibrated per a standardized procedure, DQM based on BEP allows DQE from multiple vendors to interoperate

## Slide 137: Definition of DQM
BEP | LR | DQM | Q
0.5 | 1.00 | 0 | 0.00
1E-01 | 1.11111E-01 | 5211 | 0.95
1E-02 | 1.01010E-02 | 10899 | 2.00
1E-03 | 1.00100E-03 | 16382 | 3.00
1E-04 | 1.00010E-04 | 21845 | 4.00
1E-05 | 1.00001E-05 | 27307 | 5.00
1E-06 | 1.00000E-06 | 32768 | 6.00
1E-07 | 1.00000E-07 | 38229 | 7.00
1E-08 | 1.00000E-08 | 43691 | 8.00
1E-09 | 1.00000E-09 | 49152 | 9.00
1E-10 | 1.00000E-10 | 54613 | 10.00
1E-11 | 1.00000E-11 | 60075 | 11.00
1E-12 | 1.00000E-12 | 65535 | 12.00
Start with BEP, derived within demod
Likelihood Ratio (LR) = (1 - BEP) / BEP
DQM = min (round (log10 (LR) / 12 * (2^16)), 2^16 -1)
  16-bit unsigned integer, ranges from 0 to 65,535
Easily reversed:
  LR = 10^(-12 * DQM / 2^16)
  BEP = 1 / (1 + LR)
Define “Q” as the “User’s DQM”
  Q = 12 * DQM / 65535
  Represents the exponent of 10 in the BEP
  Examples:
    Q = 3  BEP = 1e-3
    Q = 7  BEP = 1e-7

## Slide 138: DQE Format
Payload data
User selectable length, (128 ≤ N ≤ 16,536)
Defaults to 4096
16-bit
Sync
Pattern
12-bit
Word
16-bit
DQM
N bits of payload data (128 ≤ N ≤ 16,536)
4-bit Ver
Header
16-bit sync pattern (0xFAC4)
  MSB first: 1111101011000100
12-bit word, reserved for future use (currently 0)
4-bit IRIG 106 version number
16-bit DQM

## Slide 139: DQM Parameter Trades
Choice of N impacts both DQM update rate and network efficiency
4096 (default)
4096 (default)

## Slide 140: DQE Stream Builder
Insert DQM value
16-bit value that indicates the BEP for a ‘single’ block of data bits
Periodically inserted in TM data output stream
Some receivers can do DQE and non-DQE simultaneously
DQM
Estimator
DQE
Packetizer
TM Data
Receive
Antenna
RF
Quality
Information
DQM
value
TM Data + DQM
Telemetry Receiver
Test
Article
TM 0
TM 1
TM 2
TM 3
TM 0
TM 1
TM 2
TM 3
Demodulator
DQM 0
DQM 1
DQM 2
DQM 3

## Slide 141: Calibration of DQM
Calibrate DQM under various channel impairments:
AWGN – static level
AWGN – dynamic level (step response)
Dropouts
In-band and adjacent channel interference
Phase noise
Timing jitter
Multipath
Test procedures have been developed to evaluate accuracy of DQM
DQE/DQM verification test methods standardized in IRIG 118-22 V2 R2

## Slide 142: DQM Calibration Fixture
Synthesize “impaired” RF signal
Recover the “corrupted” data (with clock)
Extract the frame sync word, including DQM
Measure BER of payload data
Compare DQM (converted to BEP) to measured BER
  Recorded and analyzed on a frame-by-frame basis

## Slide 143: IRIG 118-22 Ch. 11
Defines 6 standard DQM tests
Table 11-2. Test Matrix for Data Quality Metric Testing | i
Test Number | Test Description
11.1 | BER vs BEP with Additive Noise
11.2 | DQM (BEP) Step and Dwell Response
11.3 | BER vs BEP with Adjacent Channel Interference
11.4 | BER vs BEP for Static 3-Ray Multipath Channel Conditions
11.5 | BER vs BEP for Static 2-Ray Multipath Channel Conditions
11.6 | DQM (BEP) Resynchronization Response

## Slide 144: IRIG 118-22 Ch. 11
Defines standard test fixture
Each DQE frame must be scored individually
Figure 11-1. Setup for Step Attenuator/Power Meter for BER versus BEP Test

## Slide 145: Basic AWGN Sweep

## Slide 146: Basic AWGN BER v. BEP

## Slide 147: Step AWGN BER v. BEP

## Slide 148: Not All DQMs are Created Equal

## Slide 149: Assessing Telemetry Receiver Data Quality Metrics using RCC 118-22 Test Procedures
ITC 2024
Mark Geoghegan, Sean Wilson, Jim Uetrecht
Quasonix, West Chester, OH
markg@quasonix.com
Excerpted from ITC 2024 Best Conference Paper

## Slide 150: DQE Tests / Signal Types
Signal Types | DQE Block Size (bits) | Bit Rate (Mbps) | Signal Type ID
PCM/FM | 4096 | 5 | ST1
SOQPSK | 4096 | 20 | ST2
STC | 3200 | 10 | ST3
ARTM-CPM | 16384 | 15 | ST4
SOQPSK-LDPC (r=2/3 k=4096) | 4096 | 20 | ST5
SOQPSK-LDPC (r=4/5 k=1024) | 1024 | 5 | ST6
SOQPSK-LDPC (r=1/2 k=4096) | 4096 | 5 | ST7
STC-LDPC (r=2/3 k=4096) | 4096 | 5 | ST8
DQE Test
11.1 AWGN
11.2 Step & Dwell
11.3 ACI
11.4 MP 3 Ray
11.5 MP 2-Ray
11.6 Resync
6 Tests
8 Signal Types
48 Combinations
x
Cannot verify all modulation/coding/block size/bit rate combinations (objective is functional interoperability NOT design verification)
8 representative signal types were agreed upon for DQE/DQM testing after RCC meeting with receiver vendors and Govt personnel
=

## Slide 151: Automated Testing Approach
Each Signal Type is run through all 6 tests (11.1-11.6)
Repeat with remaining Signal Types until all 48 combinations are complete
Figure 2: Example of DQE 11.1-11.6 automated testing (DQM/BEP vs Time)

## Slide 152: 11.1 AWGN
BER vs BEP/DQM in AWGN
DQM correlation is tight (Worst case Qrms = 0.38)
Averages values match very well
All 8 Signal Types are shown
Q=4.5 => 10-4.5 =>BEP=3.16e-5
A) DQM/BEP vs Time
B) Average BER/BEP vs AWGN
C) DQM Correlation

## Slide 153: 11.2 Step & Dwell
BER vs BEP/DQM in dynamic AWGN
DQM correlation is tight (Worst case Qrms = 0.43)
Step response quickly indicates changes in channel (1 DQE frame)
All 8 Signal Types are shown
A) DQM/BEP vs Time
B) DQM Step Responses
C) DQM Correlation

## Slide 154: Industry Day 2 DQE/DQM Assessment Testing
Friday Oct 25th, 2024 Meeting room Cascade B (Renaissance Hotel)

## Slide 155: Test Setup

## Slide 156: Equipment

## Slide 157: 11.1 (AWGN) Report

## Slide 158: 11.2 (Step & Dwell) Report

## Slide 159: 11.3 (ACI) Report

## Slide 160: 11.4 & 11.5 (Multipath) Report

## Slide 161: 11.6 (Resync) Report

## Slide 162: Adaptive Equalization

## Slide 163: Multipath is Ugly
Equalization can turn
Actual multipath from aircraft on the tarmac at Edwards AFB
This…
…into…
This!

## Slide 164: Adaptive Equalization
Presto! You have an adaptive equalizer
Can repair damage done by multipath
Works with a single receiver
Requires no bandwidth expansion
Requires no changes to the transmitter
Consider the multipath channel to be a filter
Varies over time
Consider building a filter which “undoes” the filtering imposed by the channel
Let it keep track of the the channel and continuously adapt itself to the channel

## Slide 165: Generic Adaptive Equalizer
Equalizer
Decision
Device
Equalizer
Adjustment
Error
Calculation
Training
Sequence
Symbol
Statistics
Training Mode
Blind Mode
Decision-Directed Mode
Transmitted Signal
Received Signal
Recovered
Data
Equalized
Signal
Error
Tap Weights
RF
Channel

## Slide 166: Adaptive Equalization, PCM/FM

## Slide 167: Adaptive Equalization, SOQPSK

## Slide 168: Adaptive Equalizer Summary
Adaptive equalizer can “undo” multipath distortion
Requires no changes at the transmit end
  If available, a training sequence can be helpful
Effectiveness of equalizer depends on the severity of the multipath
Well-designed equalizers monitor their own performance, and disengage when they are doing badly.
  This must be done without losing bit count integrity
If you have multipath, use an equalizer!

## Slide 169: Performance Evaluation of Adaptive Equalizers

## Slide 170: DQM Calibration Fixture
Synthesize “impaired” RF signal
Recover the “corrupted” data (with clock)
Extract the frame sync word, including DQM
Measure BER of payload data
Compare DQM (converted to BEP) to measured BER
  Recorded and stored on a frame-by-frame basis

## Slide 171: Test Procedure
Set frequency, modulation, and bit rate
Turn the equalizer off
Set Eb/N0 to 20 dB
Set direct path to delay 0, amplitude 1, angle 0
Enable multipath
Set reflected path delay and amplitude
Loop through delayed path phase
  0 degrees to 360 degrees in 10 degree steps
  Record DQM at each step, or record BER and calculate DQM
  Plot DQM versus phase in polar form
Turn equalizer on and repeat
  If two test units are available, test EQ on and EQ off at the same time

## Slide 172: Grading the Tests
Measure BER with EQ on and off, then compute DQM
If your DQM is well calibrated, measure DQM directly
Plot DQM vs. delay path phase, in polar form
Radius = DQM
Angle = phase of delayed path
Result will be a distorted “hoop”
Bigger radius is better
Some angles will be worse than others
Compute the area of each “hoop” for EQ on and off
“Equalizer Benefit” = Areaon – Areaoff
Since the radius is (essentially) the logarithm of the BER, the difference is the number of orders of magnitude improvement in BER

## Slide 173: DQM Calibration

## Slide 174: No Multipath, No Problem

## Slide 175: 0-100-0.9

## Slide 176: 90-100-0.9

## Slide 177: 180-100-0.9

## Slide 178: 270-100-0.9

## Slide 179: Test Results Examples

## Slide 180: 10 Mbps SOQPSK, 1 bit Delay

## Slide 181: 10 Mbps SOQPSK, 2 Bits Delay

## Slide 182: 10 Mbps SOQPSK, 5 Bits Delay

## Slide 183: 10 Mbps SOQPSK, 10 Bits Delay

## Slide 184: 10 Mbps SOQPSK, 20 Bits Delay

## Slide 185: What About Dynamics?
Figure of merit becomes the “Break Frequency” of the equalizer
Most pronounced effect of target motion is variation in phase of the reflected path
Manifests as spectral nulls sweeping through spectrum
Proposal:
Stress the equalizer by sweeping the null faster and faster, until the EQ benefit starts to drop.
Similar to the Break Frequency test for combiners

## Slide 186: What Can we Measure?
Measure the BER, averaged over all phases
  Correlates with moving test article
  Convert to DQM
  Or measure DQM, but average it correctly (see next slide)
For consistency with the static plots, plot DQM versus “spin rate”
Plot multiple delay path amplitudes on one chart
Separate charts for each delay value

## Slide 187: Equalizer Break Frequency

## Slide 188: Best Channel Selector (BCS)
Handling the “Un-Combinable” Signals

## Slide 189: Receive Diversity – Combiner
Polarization, frequency, or short-range spatial diversity
Maximal Ratio Combiner sums input channels proportional to their SNR
  Optimal in additive white Gaussian noise (AWGN) – up to 3 dB gain
  Use as only receiver output?
Notes: Receive diversity uses multiple different copies of received data to minimize the chance of data dropouts or bit errors
This diagram shows two common forms of receive diversity:
Three receivers feeding a Best Source Selector, and two received signals feeding each receiver
These signals may have different polarization, different frequencies, or come from different antennas
…

## Slide 190: Combiner Structure
how good?
make sure we can sum coherently
sum (more of the better, less of the worse)
Maximal ratio combining
Notes: To answer that question, let’s look at how a combiner works
…
So, what could possibly go wrong?

## Slide 191: Combiner Performance
Maximal ratio combining issues
Inaccurate SNR estimation: multiple signal copies, little or no noise
Degraded time and phase alignment
Downstream demodulator must deal with all received reflections
n1 reflections
n2 reflections
n1+n2 reflections
Notes: …

## Slide 192: Receive Diversity – BCS
Like a mini-BSS inside the receiver
Selects and outputs best data from just three sources (Channel 1, Channel 2, and Combiner)
Optimized for this narrowly scoped role
Notes: To address those shortcomings, we introduce the concept of a Best Channel Selector
…

## Slide 193: BCS Structure
3-channel correlating selection
line up bits from all channels
select best bit based on best DQM
“hit-less” – no dropped or duplicated bits
Notes: Like a BSS…
…

## Slide 194: BCS Test – Multipath
Apply severe multipath, engage adaptive equalization
BCS outperforms all channels
Notes: BCS has been subjected to numerous tests in the lab as well as months of use in the field
Here’s just one example
…

## Slide 195: BCS Test – Multipath
DQM reduction of 1 = BER increase of 10x (!)
BCS selection > 1000x faster than display
Combiner DQM
BCS DQM
Notes: …

## Slide 196: Field Test Results – Circle, 50º Bank, ARTM CPM, Single Antenna
Combiner performs well under stress
BCS outperforms all channels, including Combiner
  Selects data from underperforming channels at appropriate times
  Reduces bit errors and increases link availability
Notes: Accumulated errors shows where dropouts and other data loss occurred.
Link availability shows the percentage of usable seconds of telemetry data. (Fewer errors accumulated constantly may be worse than more errors accumulated in a single burst.)
In this case, the primary impairment is shading and reflections from aircraft.
…

## Slide 197: Field Test Results – Circle, 50º Bank, ARTM CPM, Single Antenna, estimated by DQM
DQM is extremely accurate – a recurring theme
DQM can be used in place of BER measurements
  Unknown data, encrypted data
DQM can be relied upon for source selection
Notes: …

## Slide 198: Field Test Results – Circle, 10º Bank, SOQPSK, Dual Antenna
Combiner performance still good
Even more improvement for BCS
  Reduces unusable seconds from 10.7% to just 2.3%
Notes: In this case, the primary impairment is self-interference from the two transmit antennas.
…

## Slide 199: Field Test Results – Circle, 10º Bank / Multipath Corridor, STC Dual Antenna
Combiner has higher error rate than CH1
Using Combiner only would have given correspondingly poor telemetry data
This illustrates the primary reason for BCS
Notes: …

## Slide 200: Field Test Results – Rocket Launch, BPSK
Combiner has higher error rate than CH1
Combiner has worse link availability than CH1 and CH2
BCS maintains nearly perfect link availability
Notes: In this case, the primary impairments are multipath at launch, and antenna shading and plume effects after launch.
…

## Slide 201: Field Test Results – Up/Down Runway, SOQPSK/LDPC
Combiner has worse link availability than CH1
BCS, selecting from three mediocre channels, provides reasonably good performance
Notes: In this case, the primary impairment is severe multipath.
…

## Slide 202: Conclusions
Combiner best most of the time, but not always
BCS mitigates cases where Combiner falls short
Uses DQM to form reliable selection criterion
Dynamically selects best data from Channel 1, Channel 2, or Combiner
  Preserves combiner gain in AWGN
  Supplements combiner in multipath, interference, etc.
Generates output with accurate composite DQM
Provides single output from dual-channel receiver that reliably supplies data superior to best channel, including Combiner
BCS does not replace BSS
BCS has great performance local to one receiver
BSS extends performance range-wide with multiple receive sites
Notes: …

## Slide 203: Best Source Selection
Short Break

## Slide 204: Combining Multiple Sources
Receive and demodulate the same signal at multiple receive sites
Funnel all the demodulated data to one central location
Time align the multiple data streams
Build a better output stream from the multiple input streams

## Slide 205: Selection Algorithms
Best Source
Maximum Likelihood Bit Detection (MLBD)
Uses log-likelihood ratio
Uses all the bits
Works with encrypted data
Max-likelihood (optimal) combining scheme
  Rice, Michael and Perrins, Erik. "Maximum Likelihood Detection From Multiple Bit Sources", Proceedings of the International Telemetering Conference, Las Vegas, NV, USA, 2015.
Majority vote
Reasonably effective with three or more sources
Reduces to guesswork with only two sources
Sub-optimal for any number of sources
Can be worse than Best Source
Based on “side information”
Never better than the best source

## Slide 206: Best Source Algorithm
Signal strength
Assumes “louder” is better
SNR
May be more useful than signal strength
Requires significant DSP for accuracy
DQM
Best option if DQM is available and accurate
PCM frame header accuracy
Uses only a small fraction of the bits to make an estimate
Poor resolution (BER is typically measured as Number of errors ÷ 32)
Useless with encrypted data
As the name implies, just pick the “best”, using…
Never better than the best available source!

## Slide 207: Majority Vote Algorithm
Assumes all voters are equally “well informed”
  All sources are equally weighted
Relatively simple to implement
Not useful with only two sources
Suboptimal for any number of sources
Benefits from “voter screening”
  Exclude sources that are not “good enough”
Can yield worse data than Best Source if some sources are poor
  Equivalent to letting uninformed voters go to the polls

## Slide 208: Max Likelihood Bit Detection
Rice, Michael and Perrins, Erik. "Maximum Likelihood Detection From Multiple Bit Sources", Proceedings of the International Telemetering Conference, Las Vegas, NV, USA, 2015.
Telemetry links suffer from a wide range of impairments
Noise
Interference
Multipath
Shadowing
Loss of antenna track
We need a way to assess the impact of all these impairments
We need to compute pn
  Quickly
  Accurately

## Slide 209: Data Quality Encapsulation
Quasonix has developed and shared an open DQM/DQE format
Published at ITC 2015
License-free, royalty-free
RCC standard as of IRIG 106-17, Chapter 2, appendix G
Includes test procedures to evaluate DQM accuracy
Payload data is bundled with its DQM, to give Best Source Selectors a valid basis for “best”
Interoperability among vendors requires standards
DQM calibration against multiple signal impairments
DQE packet structure

## Slide 210: Best Source Selection

## Slide 211: Majority Vote

## Slide 212: Max Likelihood Bit Detection

## Slide 213: Majority Vote with Dumb Voter

## Slide 214: BSS Summary
Correlating (time-aligning) source selectors deliver output data that is better than any single input stream
Combats all forms of signal impairment
Noise
Multipath
Interference
Shadowing
Loss of antenna track
Diversity can be in any form
Polarization
Frequency
Spatial
Accurate DQM with Max Likelihood Bit Detection…
Yields optimal results

## Slide 215: Rx/TX DSP Techniques

## Slide 216: Rx/Tx DSP Techniques
If you can choose your transmitter…
Space-time coding (STC)
Mitigates “built-in” multipath from dual TX antennas
Requires dual transmitters
Forward error correction
Spending bandwidth to buy link margin
Requires encoder implemented in transmitter

## Slide 217: Space-Time Coding
Eradicates Porcupines!

## Slide 218: Difficulties with TX Diversity
Spatially Separated Antennas Create Interference Pattern!
Antenna 2
Antenna 1

## Slide 219: Pattern Measurement Setup

## Slide 220: Measured Antenna Pattern

## Slide 221: Alamouti Space-Time Coding (STC)
A -B* C -D* E -F* G -H* I -J* K -L* ...
B A* D C* F E* H G* J I* L K* ...
A B C D E F G H I J K L ...
STC
Traditional
1st block
2nd block
A B C D E F G H I J K L ...

## Slide 222: Symbol Error Rate - QPSK
For Alamouti signaling
Only magnitudes of
transfer functions
used in sum
Addition of transfer
functions leads to
reduction in effective
SNR
For Alamouti signaling

## Slide 223: Antenna Pattern Interpretation
Consider BPSK Signaling and Assume s1 = s2 = 1
Time Slot 1:
Gain Pattern:
Time Slot 2:
Gain Pattern:

## Slide 224: SER Simulations
Circular Polarization Diversity Reception
Results Identical to Single Receive Antenna System

## Slide 225: Flight Tests: Airborne Configuration
10 W
10 W
STC
Transmitter
SOQPSK
Transmitter
L-band
isolator
+
+
÷
Channel Microwave
L320I
3 dB
3 dB
Pasternak
PE 7016-3
Narda 4322-2
upper antenna
lower antenna
10 W
5 W
5 W
5 W
5 W
SOQPSK
Transmitter
GPS/AHRS
house keeping link antenna
(separate lower antenna)
Quasonix
QSX-VLT-110-105-20-6A
Quasonix
Channel Microwave
L320I
L-band
isolator
Channel Microwave
L320I
L-band
isolator
Channel Microwave
L320I
L-band
isolator
Channel Microwave
L320I
Narda 4322-2
Narda 4322-2
L-band
isolator
Channel Microwave
L120I
Pasternak
PE 7016-3

## Slide 226: C-12 Beechcraft: Airborne Platform

## Slide 227: STC Video Clip

## Slide 228: M1: Test Results

## Slide 229: M2: Test Results

## Slide 230: M3: Test Results

## Slide 231: M4: Test Results

## Slide 232: M3 to C2 Transition Test Results

## Slide 233: C2: Test Results

## Slide 234: D2: Test Results

## Slide 235: STC Summary
Dual-Antenna Diversity Scheme
Realtime hardware flight tested at Edwards AFB and showed substantial performance benefit
Removes dropouts created by multiple transmit antennas
SNR equivalent to single antenna transmission
Multi-antenna scheme alleviates masking during maneuvering
Can be used with diversity reception

## Slide 236: Forward Error Correction

## Slide 237: Forward Error Correction
Basic premise
Insert redundant bits into transmitted stream
Use known relationships between bits to correct errors
Countless schemes have been developed
Convolutional code / Viterbi decoder
Block codes
  BCH
  Reed-Solomon
Concatenated codes
  RS / Viterbi
  Turbo product codes (TPC)
Low Density Parity Check (LDPC)

## Slide 238: LDPC Codes - History
LDPC: Low Density Parity Check
Linear block codes
  Some are systematic
Developed by Robert G. Gallager at M.I.T. in 1960
  Published by the M.I.T Press as a monograph in 1963
No practical implementations at that time
Re-discovered by David J.C. MacKay in 1996
  Began displacing turbo codes in the late 1990s
Recent history
2003: LDPC code selected for the new DVB-S2 standard for the satellite digital TV
2006: LDPC code selected for 10GBase-T Ethernet (10 Gbps over twisted-pair cables)
2007: LDPC codes published by CCSDS as an “Orange Book”
2008: LDPC code selected for the ITU-T G.hn standard
2009: LDPC codes adopted for Wi-Fi 802.11 High Throughput (HT) PHY specification
2012: LDPC code selected for integrated Network Enhanced Telemetry (iNET)

## Slide 239: LDPC AR4JA Codes
AR4JA: Accumulate-Repeat-4-Jagged-Accumulate
Published by CCSDS as an “Orange Book”
  Low Density Parity Check Codes For Use in Near-Earth and Deep Space Applications
Defines a family of systematic LDPC codes
Defines attached sync markers (ASM)
  Specified in section 6 of CCSDS Recommended Standard CCSDS 131.0-B-1
Present work based on the (6144, 4096) code
Information Block Length, k | Code block length n |  | 
 | Rate 1/2 | Rate 2/3 | Rate 4/5
1024 | 2048 | 1536 | 1280
4096 | 8192 | 6144 | 5120
16384 | 32768 | 24576 | 20480

## Slide 240: Packet Assembly
A
A
Ā
A
4096 Data Bits
2048 Parity bits
Input 4096 data bits
  Randomize prior to encoding, if necessary
Compute and append 2048 parity bits
Prepend 256-bit attached sync marker (ASM)
  Yields a 6400-bit packet
  Each and every code word carries the ASM: A, A, Ā, A
    A = FCB88938D8D76A4F
    Ā = 034776C7272895B0
Synchronization requires at most one code word

## Slide 241: Spectral Characterization

## Slide 242: Fractional Out-of-Band Power

## Slide 243: Decoder
Initialize decoder
Execute decode iterations until next code word
Coding gain varies with bit rate
Demodulate SOQPSK with soft decisions
Implemented 8-bit decisions
  Iterative decoders work best with high resolution soft decisions
Estimate Eb/N0 for soft decision scaling
Correlate for ASM with hard decisions
Resolves the 4-ary phase ambiguity in SOQPSK
Virtually certain sync at Eb/N0 = 0 dB

## Slide 244: Measured BER Results

## Slide 245: LDPC from Appendix 2-D
Table D-11. Bandwidth Expansion Factor | i |  | 
Information Block Length, k | Bandwidth Expansion Factor |  | 
 | Rate 1/2 | Rate 2/3 | Rate 4/5
1024 | 33/16 | 25/16 | 21/16
4096 | 33/16 | 25/16 | 21/16

## Slide 246: BER – All Modes

## Slide 247: Conclusions
SOQPSK with LDPC offers a reasonable trade of spectral efficiency for a significant gain in detection efficiency
Rate 2/3 LDPC code yields ≈9 dB coding gain relative to uncoded SOQPSK
±0.5 dB, depending on data rate
256-bit ASM provides reliable, fast synchronization at Eb/N0 < 0 dB
Synchronization is consistently achieved in < 4096 data bits
Bandwidth expansion of 25/16
Still 22% less bandwidth than legacy PCM/FM
5 other LDPC codes offer similar trade of bandwidth for BER performance

## Slide 248: LDPC for ARTM Tier 0
https://people.eecs.ku.edu/~perrins/pubs/tr/LdpcCpmReport.pdf

## Slide 249: LDPC for ARTM Tier II
https://people.eecs.ku.edu/~perrins/pubs/tr/LdpcCpmReport.pdf

## Slide 250: How Well Does It All Work Together?
Yuma Proving Grounds, AZ
Feb 8-11, 2016

## Slide 251: Recipe for Delivering Every Bit
Space Time Coding (STC)
Eliminates aircraft pattern nulls
Low Density Parity Check (LDPC) coding
Improves margin, stops “dribbling errors”
Adaptive Equalization (for non-STC signals)
Mitigates multipath
Spatial diversity with correlating source selection
Eliminate coverage-based dropouts
Requires DQE/DQM for optimal operation
TMoIP makes delivery easy

## Slide 252: Multiple Receiving Sites
Best Source Selector used 6 inputs: Ch1, Ch2 from each source, but not the combiner outputs (not enough channels).

## Slide 253: Dual Transmitter – S band – 10 W each output
Installed in UH-1 (Huey) helicopter with top and bottom blade antennas

## Slide 254: YPG Test Sites
Site CM4
Site 2
Site 4
Laguna Airfield
Site 4 to Site CM4 = 14.25 mi

## Slide 255: Analysis using Data Logs
Ch1, Ch2
DQE
Ch1, Ch2
DQE
Ch1, Ch2
DQE
Site 4
‘Best’
F1
Ch2
F2
Site 2
F1
Ch1
Ch2
F2
CM4
F1
Ch1
Ch2
F2
F1
Top
Antenna
F2
Bottom
Antenna
Receiver Analyzer BERT Log
Receiver Analyzer Log (BER of A-CSS output)
A-CSS Log
(BEP of each time-aligned source)
Data Log on
Each Receiver
(BEP, BER, RSSI,...)
Transmit F1-Top, F2-Bottom
3 Receive Sites
6 Clock & Data streams provided to A-CSS with Data Quality Encapsulation (DQE)
DQE = Receiver inserts periodic estimate of instantaneous BEP
Items of interest
  Top vs Bottom Antenna
  Individual Site Performance
  Source Selector Performance
Ch1

## Slide 256: Flight 1 – PCM/FM 5 Mbps
Link Availability Summary (PN23 BER)

## Slide 257: Flight 2 – SOQPSK 5 Mbps
Link Availability Summary (PN23 BER)

## Slide 258: Flight 3 – SOQPSK 20 Mbps
Link Availability Summary (PN23 BER)

## Slide 259: Flight 4 – STC/LDPC 5 Mbps
Link Availability Summary (PN23 BER)

## Slide 260: The elusive zero-error link…..
STC/LDPC from 3 sites at 5 MBPS
1st pass PN23 -- 34 minutes of helicopter flight across YPG…
Error-free!
2nd pass video with no freeze ups or blackouts!

## Slide 261: Performance Comparison and Summary

## Slide 262: Power Spectral Densities

## Slide 263: Out-of-Band Power

## Slide 264: BER Performance Comparison

## Slide 265: Bandwidth-Power Plane
16-APSK

## Slide 266: But Wait, There’s More!
16-APSK

## Slide 267: Acknowledgements
Mark Geoghegan
Quasonix
Kip Temple
ARTM, Edwards AFB
Bob Jefferis
Tybrin, Edwards AFB
Vickie Reynolds
White Sands Missile Range
Dr. Michael Rice
Brigham Young University
Gene Law
NAWCWD, Pt. Mugu

## Slide 268: Questions/Comments