## Slide 1: Telemetry Smorgasbord
A Little Taste of Everything
Terry Hill, Quasonix
Spring 2020

## Slide 2: Course Outline – Day 2
Demodulation
  Trellis vs. Single-Symbol
  Data Quality Metric
  Diversity Combining
  Synchronization
Channel Impairments
  Adjacent Channel Interference
  Multipath Propagation
Impairment Mitigation Techniques
  Adaptive Equalization
  Best Source Selection

## Slide 3: Side by Side Summary
Tier | M | i | h | g(t) | 99.9% BW
0 | 2 | {-1, +1} | 0.7 | Normalized impulse response of a high order Bessel filter with 3 dB bandwidth = 0.7 * bit rate | 2.03
I | 3 | {-1, 0, +1} | 0.5 | Normalized windowed impulse response of a spectral raised cosine, 8 bits long | 0.98
II | 4 | {-3, -1, +1, +3} | {4/16, 5/16} | Normalized raised cosine, 3 symbols (6 bits) long | 0.75

## Slide 4: BER Performance Comparison

## Slide 5: Today’s Modulation Tour

## Slide 6: Data Quality Metric (DQM)

## Slide 7: How to Assess Data Quality
Measured BER is not practical
  Requires known data in the stream – not possible with encryption
  Takes a long time to measure low BERs
Bit error probability (BEP), however…
  Does not require any known data
  Can be determined quickly and accurately from demodulator statistics
  Is an unbiased quality metric, regardless of channel impairments
  When calibrated per a standardized procedure, DQM based on BEP allows DQE from multiple vendors to interoperate
Each vendor can use their own algorithm for developing BEP
DQM is calculated directly from BEP
  Use of Likelihood Ratio leads to maximum likelihood BSS algorithms
  Converted to 16-bit integer on log scale

## Slide 8: Definition of DQM
Start with BEP, derived within demod
Likelihood Ratio (LR) = (1 - BEP) / BEP
DQM = min (round (log10 (LR) / 12 * (2^16)), 2^16 -1)
  16-bit unsigned integer, ranges from 0 to 65,535
Easily reversed:
  LR = 10^(-12 * DQM / 2^16)
  BEP = 1 / (1 + LR)
Define “Q” as the “User’s DQM”
  Q = 12 * DQM / 65535
  Represents the exponent of 10 in the BEP
  Examples:
    Q = 3  BEP = 1e-3
    Q = 7  BEP = 1e-7
  Arbitrarily cap Q at “a perfect 10”.
BEP | LR | DQM | Q
0.5 | 1.00 | 0 | 0.00
1E-01 | 1.11111E-01 | 5211 | 0.95
1E-02 | 1.01010E-02 | 10899 | 2.00
1E-03 | 1.00100E-03 | 16382 | 3.00
1E-04 | 1.00010E-04 | 21845 | 4.00
1E-05 | 1.00001E-05 | 27307 | 5.00
1E-06 | 1.00000E-06 | 32768 | 6.00
1E-07 | 1.00000E-07 | 38229 | 7.00
1E-08 | 1.00000E-08 | 43691 | 8.00
1E-09 | 1.00000E-09 | 49152 | 9.00
1E-10 | 1.00000E-10 | 54613 | 10.00
1E-11 | 1.00000E-11 | 60075 | 10.00
1E-12 | 1.00000E-12 | 65535 | 10.00

## Slide 9: DQE Format
Header
  16-bit sync pattern (0xFAC4)
    MSB first: 1111101011000100
  8-bit reserved word, potentially for packet header version number (currently 0)
  8-bit reserved word, potentially for source ID tag (currently 0)
  16-bit DQM
Payload data
  User selectable length, (128 ≤ N ≤ 16,536)
  Defaults to 4096
16-bit
Sync
Pattern
8-bit
Word
16-bit
DQM
N bits of payload data (128 ≤ N ≤ 16,536)
8-bit
Word

## Slide 10: Calibration of DQM
Calibrate DQM under various channel impairments:
  AWGN – static level
  AWGN – dynamic level (step response)
  Dropouts
  In-band and adjacent channel interference
  Phase noise
  Timing jitter
  Static multipath
Test procedures are being developed to evaluate accuracy of DQM
  Targeted for inclusion in IRIG 118

## Slide 11: DQM Calibration Fixture
Synthesize “impaired” RF signal
Recover the “corrupted” data (with clock)
Extract the frame sync word, including DQM
Measure BER of payload data
Compare DQM (converted to BEP) to measured BER
  Recorded and stored on a packet-by-packet basis

## Slide 12: DQM Calibration in AWGN
Required as a baseline for all other tests

## Slide 13: DQM Step Response
Assesses timeliness of DQM values
UUT stays synchronized during test
One block at each step is a blend of the two states

## Slide 14: DQM Fade Recovery
Includes UUT synchronization time

## Slide 15: DQM Interference Test
Interference is not AWGN, but it causes bit errors

## Slide 16: Diversity Combining

## Slide 17: Maximal Ratio Combining
Many telemetry systems utilize diversity reception
  Frequency separation using two transmitter
  Orthogonal polarizations using cross-polarized antenna feeds
Combining two (or more) copies of the same signal
  Diversity combining
  Creates a third signal to be demodulated
  BER performance of third signal is better than either of the individual signals
Special case – the leading use of diversity
  Linearly polarized transmit antenna on test article – could be at any orientation
  Left-hand and right-hand circularly polarized receive antennas
  Each receive antenna loses half the transmit power
  Diversity combiner puts it all back together, eliminating the polarization loss
  Frequency diversity works the same way, but uses twice the bandwidth

## Slide 18: Maximal Ratio Combining
Weight each signal in proportion to its SNR and add
Yields optimum SNR on combined channel in AWGN
SNRcombined = SNRa + SNRb

## Slide 19: Maximal Ratio Combining
Jump to file: diversity-combiner-video.mp4
  Or, click to view on our website: Combining Video

## Slide 20: BER Results - Fading Signals

## Slide 21: Measured Combiner BER - Tier 0

## Slide 22: Measured Combiner BER - Tier I

## Slide 23: Measured Combiner BER - Tier II

## Slide 24: Combiner Summary
Receive-side processing
  No transmitter impact
Phase aligns the signals
Forms weighted sum of two inputs
SNR of the weighted sum is at least as high as the better signal
May be as much as 3 dB higher (equal input case)
Conventional combiner design assumes signals are time-aligned
  Performance falls off rapidly with increasing time skew
  Combiner will probably fail altogether at ± ½ bit time skew
Some combiners do both phase alignment and time alignment
  Supports operation with spatially separated antennas
If you have access to two copies of the signal, use them!

## Slide 25: Synchronization

## Slide 26: Telemetry Channels are Bursty
Figure from Robert Jefferis, Tybrin, Edwards AFB. Reprinted by permission of the author.
Synchronization is important!
In a typical flight test, the vast majority of bit errors occur at dropouts

## Slide 27: Synchronization Test
IRIG 118-12, Procedure 7.4 (Flat Fade Recovery Test)
Transmit randomized ones pattern
Measure time at which output becomes “all (or mostly) ones”
IRIG
Randomizer
Modulator
Add Noise
Noise
Switch
Demod
with
Derandomizer
Timer
Ones
Detector
All ones
Controller
Start
Stop

## Slide 28: Typical Sync Test

## Slide 29: Synchronization Parameters
Modulation technique
  Tier 0 uses more bandwidth – easier to synchronize to
  Tier I is spectrally compact, making it slippery – synchronization is more difficult
    Trellis demodulation helps achieve sync
  Tier II is even more compact – synchronization takes longer
Bit rate
  Fixed-duration tasks amount to more bits at high bit rates
Signal to noise ratio
  Sync times will be longer at low SNR
Synchronization threshold
  SNR at which the demodulator can acquire sync
Sync loss threshold
  SNR at which a synchronized demodulator will drop sync

## Slide 30: Tier 0 Synchronization
Channel 1, 2
Combiner

## Slide 31: Tier I Synchronization
Channel 1, 2
Combiner

## Slide 32: Tier 0 Synchronization
Channel 1, 2
Combiner

## Slide 33: Low SNR Synchronization

## Slide 34: Synchronization Summary
The aeronautical telemetry channel is plagued with dropouts
Rapid synchronization, and synchronization at low SNR, is the best means of minimizing the impact of these dropouts
IRIG 118 defines test procedures for measuring sync time and sync thresholds
Pay attention to synchronization performance!

## Slide 35: Adjacent Channel Interference

## Slide 36: PSD is Half the Story
Overall spectral efficiency is determined by spacing between channels
Receiver selectivity affects channel spacing
A valid comparison must account for both transmitted spectrum and “tolerable” receiver filtering
Not all modulations are equally “tolerant” of IF filtering and interference
Multi-channel testing accounts for these factors

## Slide 37: Multi-channel ACI Test Set

## Slide 38: 9 Mbps Multi-h CPM, Multichannel

## Slide 39: BER as a Function of F
From Gene Law, “Recommended Minimum Telemetry Frequency Spacing With CPFSK, CPM, SOQPSK, and FQPSK Signals”, ITC 2003

## Slide 40: Degradation as a Function of F
From Gene Law, “Recommended Minimum Telemetry Frequency Spacing With CPFSK, CPM, SOQPSK, and FQPSK Signals”, ITC 2003

## Slide 41: ACI Summary
I/C=20 dB
From Gene Law, “Recommended Minimum Telemetry Frequency Spacing With CPFSK, CPM, SOQPSK, and FQPSK Signals”, ITC 2003

## Slide 42: Frequency Separation Rule
where:
  • ΔF0 = the minimum center frequency separation in MHz
  • Rs = bit rate of desired signal in Mb/s
  • Ri = bit rate of interfering signal in Mb/s
ΔF0 = as*Rs + ai*Ri
The NRZ PCM/FM signals are assumed to be premodulation filtered with a multi-pole filter with 3 dB point of 0.7 times the bit rate and the peak deviation is assumed to be approximately 0.35 times the bit rate.
The receiver IF filter is assumed to be no wider than 1.5 times the bit rate and provides at least 6 dB of attenuation of the interfering signal.
The interfering signal is assumed to be no more than 20 dB stronger than the desired signal.
The receiver is assumed to be operating in linear mode; no significant intermodulation products or spurious responses are present.

## Slide 43: Multipath Propagation
Brace yourself!
Greek symbols ahead!

## Slide 44: Multipath Propagation
Dry lake bed = smooth reflecting surface
Narrow beam receive antenna
Airborne transmitter
Line-of-sight communications link
Irregular terrain
Low elevation angle
Figure from Dr.Michael Rice, BYU Telemetry Laboratory, Provo, Utah. Reprinted by permission of the author.

## Slide 45: Assumptions
Channel can be modeled as a linear time-invariant (LTI) system over “short enough” time interval
Line-of-sight propagation path
L-1 multipath propagation paths
Figure from Dr.Michael Rice, BYU Telemetry Laboratory, Provo, Utah. Reprinted by permission of the author.
Complex-valued path loss

## Slide 46: 2-Ray Transfer Function
Magnitude of first multipath reflection: G1
“sweep rate” of multipath null ~
(dB)
1 (0 dB)
Figure from Dr.Michael Rice, BYU Telemetry Laboratory, Provo, Utah. Reprinted by permission of the author.

## Slide 47: 3-Ray Transfer Function
1 (0 dB)
M
D
(dB)
(3-Ray Model)
(dB)
(2-Ray Model)
Figure from Dr.Michael Rice, BYU Telemetry Laboratory, Provo, Utah. Reprinted by permission of the author.

## Slide 48: Multipath on the Tarmac
Nearly static, frequency selective, long delays

## Slide 49: Multipath in Flight
Dynamic, frequency selective and flat fading, various delays

## Slide 50: Multipath Summary
If your test article operates near the ground, you are quite likely experiencing multipath.
If so, there will be intervals during which no useful data is recovered.
Loss of bit count integrity is likely
  Encrypted links will lose crypto sync
What to do?
Stay tuned for the “Adaptive Equalizer” discussion

## Slide 51: Adaptive Equalization

## Slide 52: Multipath is Ugly
Equalization can turn
this into… this.
Actual multipath from aircraft on the tarmac at Edwards AFB

## Slide 53: Adaptive Equalization
Consider the multipath channel to be a filter
  Varies over time
Consider building a filter which “undoes” the filtering imposed by the channel
  Let it keep track of the the channel and continuously adapt itself to the channel
Presto! You have an adaptive equalizer
  Can repair damage done by multipath
  Works with a single receiver
  Requires no bandwidth expansion
  Requires no changes to the transmitter

## Slide 54: Equalizer Techniques
J.G. Proakis, Digital Communications. 1989 2nd Edition

## Slide 55: Generic Adaptive Equalizer
Equalizer
Decision
Device
Equalizer
Adjustment
Error
Calculation
Training
Sequence
Symbol
Statistics
Training Mode
Blind Mode
Decision-Directed Mode
Transmitted Signal
Received Signal
Recovered
Data
Equalized
Signal
Error
Tap Weights
RF
Channel

## Slide 56: Adaptive EQ - Adapting
Jump to file: equalizer-out-pcmfm-3ray-dynamic-video.mp4
  Or, click to view on our website: PCMFM Adaptive Equalizer Video
Jump to file: equalizer-out-soqpsk-3ray-dynamic-video.mp4
  Or, click to view on our website: SOQPSK Adaptive Equalizer Video

## Slide 57: Adaptive Equalizer in Action
Jump to file: rdms-rackmount-receiver-adaptive-equalizer-demonstration-video.mp4
  Or, click to view on our website: Adaptive Equalizer Demonstration Video

## Slide 58: Adaptive Equalizer Summary
Adaptive equalizer can “undo” multipath distortion
Requires no changes at the transmit end
  If available, a training sequence can be helpful
Effectiveness of equalizer depends on the severity of the multipath
Well-designed equalizers monitor their own performance and disengage when they are doing badly.
  This must be done without losing bit count integrity
If you have multipath, use an equalizer!

## Slide 59: Performance Evaluation of Adaptive Equalizers

## Slide 60: So Many Channels…
Each path is characterized by
  Delay
  Amplitude
  Phase shift (potentially time-varying)
2, 3, or more paths
Modulation matters
SNR matters
Need a 10-dimensional universe to plot the results
Way too many test points

## Slide 61: Let’s Simplify
Stick to 2-ray model
  Easy to synthesize
  Still allows a range of channels from easy to impossible
  Maybe we add a third ray for a limited set of tests
Stick to one SNR
  High enough that the equalizer works on mitigating multipath, not rejecting noise
  Not so high that there are never any bit errors
  Should reflect actual use cases
  Propose 20 dB
Limited set of amplitudes and delays
Many phase angles

## Slide 62: Proposed Signal Conditions
Pick a carrier frequency
  How many?
  Nulls “sweep faster” at higher frequencies (dynamic case only)
20 dB SNR (without multipath)
Tier 0, I, and II
  Tier 0: 1, 5, 10, 20 Mbps
  Tier I and Tier II: 2, 10, 20, and 40 Mbps
Areas for further research
  STC – different multipath on each signal, hmmm….
  LDPC – six codes?

## Slide 63: Proposed Static Channels
Channel response depends on
  Carrier frequency,
  Delay,
  Reflection amplitude,
  Reflection phase,
Delays (in bits) of 0.5, 1, 2, 5, 10, 20, and 50
  Delays much shorter than 0.5 bit are essentially flat fades, where the signal power is simply gone. EQ cannot help.
Amplitudes of 0.5 to 0.9 in steps of 0.1
  For bonus points, include 0.95 and 0.98
Phases of 0° to 360° in 10° steps

## Slide 64: What is the Measured Value?
Must be observable with EQ both on and off
Bit error rate is universally understood
DQM is readily computed from BER
  With calibration, DQM is much more quickly measured
Remind me again, what is DQM?

## Slide 65: Definition of DQM (a.k.a. Q)
To a statistician, DQM is the “Log Likelihood Ratio”
Start with probability of error, P
  Be practical: 0.5 < P < 1e-12
  BEP, derived within demod
  BER, measured with a BERT
Likelihood Ratio (LR) = P / (1 – P)
Q = min (-log10(LR), 12)
Easily reversed:
  P = 10-Q / (1 + 10-Q)
Short version
  Q = 5  P = 1e-5
P | Q
0.5 | 0.000
1E-01 | 0.954
1E-02 | 1.996
1E-03 | 3.000
1E-04 | 4.000
1E-05 | 5.000
1E-06 | 6.000
1E-07 | 7.000
1E-08 | 8.000
1E-09 | 9.000
1E-10 | 10.000
1E-11 | 11.000
1E-12 | 12.000

## Slide 66: DQM Calibration Fixture
Synthesize “impaired” RF signal
Recover the “corrupted” data (with clock)
Extract the frame sync word, including DQM
Measure BER of payload data
Compare DQM (converted to BEP) to measured BER
  Recorded and stored on a packet-by-packet basis

## Slide 67: Test Procedure
Set frequency, modulation, and bit rate
Turn the equalizer off
Set Eb/N0 to 20 dB
Set direct path to delay 0, amplitude 1, angle 0
Enable multipath
Set reflected path delay and amplitude
Loop through delayed path phase
  0 degrees to 360 degrees in 10 degree steps
  Record DQM at each step, or record BER and calculate DQM
  Plot DQM versus phase in polar form
Turn equalizer on and repeat
  If two test units are available, test EQ on and EQ off at the same time

## Slide 68: Grading the Tests
Measure BER with EQ on and off, then compute DQM
  If your DQM is well calibrated, measure DQM directly
Plot DQM vs. delay path phase, in polar form
  Radius = DQM
  Angle = phase of delayed path
Result will be a distorted “hoop”
  Bigger radius is better
  Some angles will be worse than others
Compute the area of each “hoop” for EQ on and off
“Equalizer Benefit” = Areaon – Areaoff
  Since the radius is (essentially) the logarithm of the BER, the difference is the number of orders of magnitude improvement in BER

## Slide 69: DQM Calibration

## Slide 70: No Multipath, No Problem

## Slide 71: 0-100-0.9

## Slide 72: 30-100-0.9

## Slide 73: 60-100-0.9

## Slide 74: 90-100-0.9

## Slide 75: 120-100-0.9

## Slide 76: 150-100-0.9

## Slide 77: 180-100-0.9

## Slide 78: 210-100-0.9

## Slide 79: 240-100-0.9

## Slide 80: 270-100-0.9

## Slide 81: 300-100-0.9

## Slide 82: 330-100-0.9

## Slide 83: 360-100-0.9

## Slide 84: Test Results Examples

## Slide 85: 10 Mbps SOQPSK, 1 bit Delay

## Slide 86: 10 Mbps SOQPSK, 2 Bits Delay

## Slide 87: 10 Mbps SOQPSK, 5 Bits Delay

## Slide 88: 10 Mbps SOQPSK, 10 Bits Delay

## Slide 89: 10 Mbps SOQPSK, 20 Bits Delay

## Slide 90: What About Dynamics?
Most pronounced effect of target motion is variation in phase of the reflected path
  Manifests as spectral nulls sweeping through spectrum
Proposal:
  Stress the equalizer by sweeping the null faster and faster, until the EQ benefit starts to drop.
  Similar to the Break Frequency test for combiners
Figure of merit becomes the “Break Frequency” of the equalizer

## Slide 91: What Can we Measure?
Measure the BER, averaged over all phases
  Correlates with moving test article
  Convert to DQM
  Or measure DQM, but average it correctly (see next slide)
For consistency with the static plots, plot DQM versus “spin rate”
Plot multiple delay path amplitudes on one chart
Separate charts for each delay value

## Slide 92: Equalizer Break Frequency

## Slide 93: Course Outline – Day 3
Impairment Mitigation Techniques
  Adaptive Equalization
  Best Source Selection
  Best Channel Selection
  Space-Time Coding (STC)
  Low Density Parity Check (LDPC) Coding
Using All the Tools Together
Performance Comparison & Summary
Link Budgets